## Slide 1: Total performance evaluation on plant factory with artificial lighting (PFAL)
Wei FANG, Ph.D., Professor
Dept. of Biomechatronics Engineering
National Taiwan University

## Slide 2: Total performance evaluation
Area required to harvest 1 kg
Photons required to harvest 1 kg
Labor required to harvest 1 kg
Electricity cost required to harvest 1 kg

## Slide 3
Tray or Plate (TorP)
Area, m2
Density, plt/TorP
Density, plt/m2
Duration, days
Area per 1000 plts
Area ratio
Area * days
Area&Time ratio
Assuming 100 g per plant, 10 plants can reach 1 kg
Area required for 1000 plants is 26.7 m2, thus
harvesting 1 kg, you need 26.7*10/1000 = 0.267 m2
Area required to harvest 1 kg of vegetable

## Slide 4
TLI = DLI * Days
DM = 0.045 * FM
FM = DM / 0.045
100 g FM * 0.045 = 4.5 g DM
45 g DM = -1.886 + 0.0132 (TLI)
TLI = 3552 mol/m2
35 days
DLI = 8.57 11.42 14.3 17.14 20 22.85
Photons required to harvest 1 kg of vegetable

## Slide 5
Labor required to harvest 1 kg of vegetable
Sowing
Spacing
Transplanting
Harvesting
Packaging
Need to have the operating time for all manual operated task.
OP.time(i) = Convert all values into per plant basis, in min/plt.
TOP.time = Sum of OP.time(i) of all task.
TOP.time * number of plants per 1 kg

## Slide 6
Electricity cost required to harvest 1 kg of vegetable
To harvest 1 kg, value of kWh needed = 1000 / EY
Where EY in g_FW/kWh (EY will be introduced later)
Given utility fee (U, in $/kWh)
Electricity cost on light to harvest 1 kg
= 1000 * U / EY
Given COP of AC,
Electricity cost on light and AC
= 1000 * U * (COP+1)/ (COP * EY)

## Slide 7: Total performance evaluation
PVr and P2Cr
PY, EY and OLe

## Slide 8
OLe = EY/PY
P2Cr
(Price / (varCost+fixCost)
EY
(g kWh-1)
PY
(g mol-1)
PVr
(Price / Varcost)

## Slide 9: photon yield (PY)
From sowing to harvest, calculate DLI of each stages (mol/m2/day), times duration of each stage to get TLI (mol/m2)
Divide TLI by the density (plts/m2) of each stage to derived mol/plt of each stages.
Sum up for all stages
Derive PY by divide the avg. harvested FM (g/plt) to (mol/plt) to derive g FM/mol.

## Slide 10
Photon Yield, PY
Daily Light Integral (DLI) in mol day-1 m-2
  PPFD (400-700 nm, PAR, μmol m-2 s-1 ) ×Light period (h d-1) ×3.6/1000
Total light integral per plant at stage i, TLI(i) in mol/plant
  TLI(i) = DLI(i) × Duration(i) / cropping density(i)
Overall Total Light Integral per plant
PY (g mol-1) = g_FW / OTLI (g/plant / mol/plant)
PYA (mg mol-1) = mg.Anthocyanin/plant / OTLI (mol/plant)
PYD (mg mol-1) = mg.Vit.E/plant / OTLI (kWh/plant)
OTLI =
Area of cultural bed
Cropping density

## Slide 11: energy yield (EY)
From sowing to harvest, calculate power consumption (PC) per unit area of each stages (kWh/m2/day), times duration of each stage to get TPC (kWh/m2), then divided by the density (plts/m2) of each stage to derived kWh/plt of each stages.
Sum up for all stages
Derive EY by divide the avg. harvested FM (g /plt) to (kWh/plt) to derive g FM/kWh.

## Slide 12
Energy Yield, EY
Area of cultural bed
Cropping density
Power consumption per unit area, PCA (W m-2)
  Power consumption per lamp (W) × number of lamps per unit area (m-2)
Daily power consumption per unit area per day, DPI (kWh d-1 m-2)
  PCA (W m-2) × light period (h d-1) / 1000
Total power integral per plant, TPI(i) (kWh/plant)
  DPI(i) × duration(i) / cropping density(i) (plant m-2)
Overall Total Power Integral per plant
OTPI =
EY (g/kWh)= gFW (g/plant) / OTPI (kWh/plant)
EYA (mg/kWh)=mg Anthocyanin (mg/plant) / OTPI (kWh/plant)
EYD (mg/kWh)= mgVit.E/plant / OTPI

## Slide 13: Details to EY calculation
  Stage 1
    duration (d):14
    Light period (h/d): 24
    Power (W) per lamp :18
    Area : 0.6 m2
    No.lamps : 7 tubes
      No.lamps/m2: 12.73 tubes/ m2
    No.plants: 433 plts
      Cropping density: 772 plt/m2
  Stage 2
    …………
TPI(1) (kWh/plant) = 14*24*18*12.73/772/1000=0.0997
TPI(i) =
EY(g/kWh)= FW (g/plant) /OTPI
OTPI =

## Slide 14
SR5
SB5
SR3SB2
SR4SB1
x5
x3 +
x2
x4+
x1
x5
bar=15
Treatment | g/plt | Anthocy. mg/g | Anthocy. Content per plant mg/plt | EY g/kWh | EYA mg/kWh | PY gFW/mol | PYA mg/mol
SR5 | 54.06 | 0.0138 | 0.74 | 47.03 | 0.65 | 11.01 | 0.15
SR3SB2 | 38.77 | 0.0168 | 0.65 | 32.29 | 0.54 | 7.89 | 0.13
SR4SB1 | 50.12 | 0.0124 | 0.62 | 42.65 | 0.53 | 10.20 | 0.13
SB5 | 22.14 | 0.0179 | 0.40 | 30.58 | 0.55 | 4.51 | 0.08

## Slide 15
SR6
SB6
SR3SB3
SR4SB2
SR5SB1
Treatments | FW gFW/plt | Anthocya. concentration mg/g | Anthocya. content mg/plt | EY gFW/kWh | EYA mg/kWh | PY gFW/mol | PYA mg/mol | OLe mol/kWh
SR6 | 108.30 | 0.0138 | 1.49 | 67.15 | 0.93 | 15.72 | 0.22 | 4.271
SR3SB3 | 70.11 | 0.0149 | 1.04 | 43.47 | 0.65 | 10.17 | 0.15 | 4.272
SR4SB2 | 88.70 | 0.0147 | 1.31 | 55.00 | 0.81 | 12.87 | 0.19 | 4.273
SR5SB1 | 87.75 | 0.0197 | 1.73 | 54.41 | 1.07 | 12.73 | 0.25 | 4.274
SB6 | 43.24 | 0.0159 | 0.69 | 26.81 | 0.43 | 6.27 | 0.10 | 4.276
Overall Lighting Efficacy, in mol/kWh
(OLe) = EY / PY
PY Photon Yield of fresh mass
PYA Photon Yield of Anthocyanin
EY Energy Yield of fresh mass
EYA Energy Yield of Anthocyanin

## Slide 16: Effects of OLED as light source to the growth and antioxidants-concentration of Taiwan jewel orchid
OLED 1
OLED 2
LED CW
Bar =10 cm
OLED 1
OLED 2
LED CW
Bar =10 cm
Treatment | g/plt | Gastrodin concentration μg/g | Gastrodin content μg/plt | DPPH concentration vit C mg/g | DPPH content mg/plt | EY g/kWh | EYG μg/kWh | EYD mg/kWh
OLED 1 | 9.6 | 12.7 | 121.3 | 0.03 | 0.28 | 6.8 | 86.3 | 0.20
OLED2 | 10.6 | 13.1 | 138.5 | 0.04 | 0.42 | 4.8 | 62.0 | 0.19
CW | 10.9 | 5.0 | 54.0 | 0.03 | 0.28 | 7.0 | 34.7 | 0.18
Treatment | PY g/mol | PYG mgGastrodin/mol | PYD mgDPPH/mol | OLe
OLED 1 | 3.17 | 40.24 | 0.09 | 2.145
OLED2 | 3.52 | 45.96 | 0.14 | 1.363
CW | 3.60 | 17.93 | 0.09 | 1.944

## Slide 17
Le in μmol/J, measured after the installation of light source prior to the growth of any plants.
OLe in mol/kWh, calculated after the growth, allow the adjustment of light source and light period during any growth stages.
If no alteration of light source during the growth period, two terms have the relationship as shown below:
Le = OLe / 3.6
Lighting Efficacy (Le) vs. Overall Lighting Efficacy (OLe)

## Slide 18
TPE diagram: PY vs. EY
Chart: 
| 52 | 76.022376747686536 | 37 | 57.016782560764909 | 36.630000000000003
 | 8 | 17.2954 | 10 | 12.9715 | 12.73
Light source has better spectrum to grow the crop
Light source has
higher efficiency and less power consumption to grow the crop
Toward optimum light source

## Slide 19
Price of the product vs. variable Cost + fixed Cost on lighting
PV ratio =
P2C ratio =
Price of the product vs. Variable cost on lighting

## Slide 20
EY
(g/kWh)
Market Value (mVal) / Electricity Fee on Lightg
蔬菜 | 價格 (元/g) | 參考
purple cabbage sprouts紫甘藍芽 | 0.9 | 綠藤生機 Green Vine, Taiwan
broccoli sprouts 青花菜芽 | 0.9 | 
Radish Sprouts 蘿蔔嬰 | 0.3 | 
Lettuce 萵苣類 | 1.0 | 庭茂 Nice Green, Taiwan
Anoectochilus roxburghii 金線連 | 15.0 | 
Rucola 芝麻葉 | 7.2 | 
Functional lettuce 機能性萵苣 (Low potassium 、high anthocyanin) | 2.0 | 日本富士通 Fujizu, Japan
Organic Lettuce 萵苣有機水耕 | 1.3 | 
PVr

## Slide 21
PVr = Pg / Vg
Vg = Ukwh / EY
where,
PVr: PV ratio, in $/$
Pg : Price per gram, in $/g
Vg : Variable cost per gram on lighting, in $/g
Ukwh : Utility.fee per kWh, in $/kWh
EY: Energy Yield, in g/kWh
PVr = Pg * EY / Ukwh

## Slide 22
Chart: 
| 616.66999999999996 | 299.23 | 217.84 | 444.82 | 396.36 | 102.12
紫甘藍芽OLED | 109 | 121 | 48 | 114 | 102 | 49
EY, PY and PVr (TPE diagram) of different sprouts
grown under various light quality
PVr is the radius of the circle

## Slide 23
Chart: 
| 52 | 76.022376747686536 | 37 | 57.016782560764909 | 36.630000000000003
 | 8 | 17.2954 | 10 | 12.9715 | 12.73
Lettuce and rucola grown under various light quality
shown on TPE diagram

## Slide 24
Chart: 
| 616.66999999999996 | 299.23 | 217.84 | 444.82 | 396.36 | 102.12 | 52 | 76.022376747686536 | 37 | 57.016782560764909 | 36.630000000000003
紫甘藍OLED | 109 | 121 | 48 | 114 | 102 | 49 | 8 | 17.2954 | 10 | 12.9715 | 12.73
Lettuce and sprout grown under various light quality
shown on TPE diagram

## Slide 25
vegetable | Artificial Light |  | EY (g/kWh) | PY (g/mol) | PVr | Relative PVr
 | Light quality | Power (W·m–2) |  |  |  | 
紫甘藍芽 | OLED | 15.8 | 617 | 109 | 231 | 7.3
紫甘藍芽 | R100 | 35.8 | 299 | 121 | 112 | 3.5
蘿蔔嬰 | R100 | 72.7 | 445 | 114 | 56 | 1.8
蘿蔔嬰 | R87:B13 | 71.5 | 396 | 102 | 50 | 1.6
青花菜芽 | R100 | 70.6 | 102 | 49 | 38 | 1.2
青花菜芽 | OLED | 31.8 | 218 | 48 | 82 | 2.6
芝麻葉 | CW | 218.18 | 21 | 9 | 63 | 2.0
香波綠萵苣 | CW | 185.14 | 75 | 17 | 32 | 1.0
紅橡萵苣 | CW | 185.14 | 37 | 10 | 15 | 0.5
皺葉萵苣 | CW | 185.14 | 57 | 13 | 24 | 0.8
紅橡萵苣 | SR5SB1 | 126.39 | 37 | 13 | 31 | 1.0
波士頓萵苣 | CW | 185.14 | 76 | 17 | 32 | 1.0
25
Impact of light quality on EY, PY and PVr

## Slide 26
Chart: 電力產能 (EY, g/kWh)
| 133.87540545267601 | 70.016608984619296 | 76.022376747686536 | 74.955053593067774 | 57.016782560764909 | 17.243731847121506 | 48.62732380888265
 | 30.4572 | 15.9291 | 17.2954 | 17.3507 | 12.9715 | 3.9293 | 11.2563
Impact of nutrient solution on TPE diagram

## Slide 27
Lettuce | Nutrient solution | EY (g/kWh) | PY (g/mol) | PVr | Relative PVr
皺葉 | BIO NK | 134 | 30 | 50 | 2.3
皺葉 | Yamazaki | 57 | 13 | 16 | 0.7
波士頓 | BIO NK | 70 | 16 | 26 | 1.2
波士頓 | Yamazaki | 76 | 17 | 22 | 1.0
香波綠 | BIO NK | 17 | 4 | 6 | 0.3
香波綠 | Yamazaki | 75 | 17 | 21 | 1.0
香波綠 | NTU_low_P | 49 | 11 | 28 | 1.3
Impact of nutrient solution on EY, PY and PVr

## Slide 28
Vege. | treatment | EY (g/kWh) | PY (g/mol) | PVr | Relative PVr | Value-added
紫甘藍 | OLED | 617 | 30 | 162 | 7.4 | 高抗氧化力
 | R100 | 299 | 14 | 78 | 3.5 | 
青花菜 | OLED | 218 | 10 | 57 | 2.6 | 高抗氧化力
 | R100 | 102 | 20 | 27 | 1.2 | 
蘿蔔嬰 | R100 | 445 | 21 | 44 | 2.0 | 
 | R87:B13 | 396 | 19 | 39 | 1.8 | 高抗氧化力
奶油萵苣 | BIO N | 49 | 11 | 18 | 0.8 | 民眾信賴
 | BIO NK | 70 | 16 | 26 | 1.2 | 
 | 山崎湛液 | 76 | 17 | 22 | 1.0 | 
 | 山崎潮汐 | 148 | 24 | 42 | 1.9 | 高產量
皺葉萵苣 | 山崎湛液 | 57 | 13 | 16 | 0.7 | 
 | BIO N | 82 | 19 | 31 | 1.4 | 民眾信賴
 | BIO NK | 134 | 30 | 50 | 2.3 | 
冰山萵苣 | 山崎湛液 | 75 | 17 | 21 | 1.0 | 
 | 低鉀萵苣 | 49 | 11 | 28 | 1.3 | 腎臟病人專用
紅橡 | CW | 37 | 10 | 10 | 0.5 | 
 | SR5SB1 | 37 | 13 | 21 | 1.0 | 高花青素
芝麻葉 | 山崎潮汐 | 52 | 8 | 107 | 4.9 | 高產量/藥味

## Slide 29
Only reflect the operating cost on electricity of lamps
Did not includes the cost to purchase the lamps
Can only be used for evaluation for cases with similar cost to purchase the lamps.
A new index was developed to include the fixed cost on lamps.
Drawbacks of PVr leads to a new index

## Slide 30
EY
(g/kWh)
PVr
Market Value (mValue) / Vari.Cost
P2Cr = mValue / (VC+FC)
From PVr to P2Cr

## Slide 31
EY
(g/kWh)
PY
(g/mol)
Market price
Cost on light source
Power consump. of light
Utility fee
Cultural practices
Factors affecting P2Cr

## Slide 32
Overall Total Depreciation of LED (OTD, NT$/plant)
Usable life of LED (h): 35000 (assuming)
Cost of light source (NT$/piece)：WW=1500 ，RB=1000，CW=390
3. OTD: Overall Totally Depreciation of LED per plant (NT$/plant)
De(i) = Plamp(i) * Noflamp(i) / Lf(i)
TD(i) = De(i) * LP(i) * Days(i) / density(i)
De(i): Depreciation of light source per unit area per hour,, in NT$ /m2 h
Plamp: Unit price of lamp, in NT$/piece
Noflamp: number of lamps required per unit area, in piece/ m2
Lf: usable life time of the lamp, in h
TD(i): Total depreciation of light source per plant in stage i, in NT$ / plant
LP(i) : Duration of light period per day, in stage i in h/day
Days(i): duration of days in stage i, in days
density(i): crop density sta stage i, in plant/m2

## Slide 33
Light source | Crop | EY (g/kWh) | PY (g/mol) | P2Cr | OTPI (kWh/plant) | Vari.Cost (NT$/plant) | OTD=FixCost (NT$/plant) | LED Cost (NT$/tube)
CW | 羽衣甘藍 | 26.6 d | 6.39 d | 2.6 | 7.69 | 26.9 | 0.9 | 390
 | 香波綠 | 37.1 c | 8.92 b | 3.7 |  |  |  | 
 | 紅皺葉 | 22.4 e | 5.38 e | 2.2 |  |  |  | 
WWP | 羽衣甘藍 | 40.7 c | 5.29 e | 3.4 | 4.16 | 14.6 | 3.3 | 1500
 | 香波綠 | 83.8 a | 10.90 a | 7.0 |  |  |  | 
 | 紅皺葉 | 68.3 b | 8.22 b | 5.7 |  |  |  | 
RB_FR | 羽衣甘藍 | 27.5 d | 6.83 d | 2.6 | 7.94 | 27.8 | 2.2 | 1000
 | 香波綠 | 40.0 c | 9.91 a | 3.8 |  |  |  | 
 | 紅皺葉 | 30.1 d | 7.47 c | 2.8 |  |  |  | 
Means followed by the different letters in each column are significantly different at 5% level by LSD Test (n=5).
Impact of types of light source and crop on index for T.P.E.

## Slide 34
羽衣甘藍
紅皺葉萵苣
2000 hr (0.3 year)
10000 hr (1.7 year)
14000 hr (2.3year)
3000 hr (0.5 year)
5000 hr (0.8 year)
香波綠萵苣
Impact of usable life of LEDs to P2Cr of 3 crops
P2Cr

## Slide 35
Chart: 
| 616.66999999999996 | 299.23 | 217.84 | 444.82 | 396.36 | 102.12 | 52 | 76.022376747686536 | 37 | 57.016782560764909 | 36.630000000000003
紫甘藍OLED | 109 | 121 | 48 | 114 | 102 | 49 | 8 | 17.2954 | 10 | 12.9715 | 12.73
Chart: 
| 616.66999999999996 | 299.23 | 217.84 | 444.82 | 396.36 | 102.12 | 52 | 76.022376747686536 | 37 | 57.016782560764909 | 36.630000000000003
紫甘藍OLED | 109 | 121 | 48 | 114 | 102 | 49 | 8 | 17.2954 | 10 | 12.9715 | 12.73
PVr as the radius of the circle.
Ignoring the fixed cost leads to mis-leading results.
P2Cr as the radius of the circle
PVr vs. P2Cr on TPE diagram

## Slide 36
Treatments | EY(g/kWh) | PVr | P2Cr | OTD (NT$/plt)
紫甘藍OLED | 617 | 231.3 | 2.4 | 226.1
紫甘藍R100 | 299 | 112.2 | 112.2 | 0.001
蘿蔔嬰R100 | 445 | 55.6 | 55.6 | 0.001
蘿蔔嬰R87:B13 | 396 | 49.5 | 49.5 | 0.001
青花菜OLED | 218 | 81.7 | 0.9 | 226.1
青花菜R100 | 102 | 38.3 | 38.3 | 0.001
皺葉BIONK | 134 | 72.5 | 51.2 | 0.86
皺葉BION | 82 | 44.6 | 31.5 | 0.86
三低冰山 | 49 | 40.5 | 29.8 | 0.86
奶油BIONK | 70 | 37.9 | 27.8 | 0.86
奶油 | 76 | 31.7 | 23.3 | 0.86
冰山 | 75 | 39.0 | 22.9 | 0.86
奶油BION | 49 | 26.4 | 19.4 | 0.86
皺葉 | 57 | 23.8 | 17.4 | 0.86
紅橡CW | 37 | 15.4 | 11.3 | 0.86
紅橡SR5SB1 | 37 | 30.5 | 22.4 | 0.86
OTD of OLED
Price: 30000 NT$/plate
Usable life: 200 h
Piece required: 400 piece/m2
Days：5 days
Duration per day：12 h
Depreciation per unit area = 30000*400*5*12/200 = 3600000 NT$/m2
Crop density: 15923 plant/m2
OTD = 3600000/15923 = 226.1
EY, PVr and P2Cr of leafy greens grown under various light quality and nutrient solution

## Slide 37: The end