## Slide 1
PFAL System Design & Engineering Economic Analysis
Wei FANG
Dept. of Biomechatronics Engineering and and Global ATGS
Center of Excellence for Controlled Environment Agriculture (CCEA)
National Taiwan University
Plant Factory – Theory and Practice
Notes: 1

## Slide 2: Outline
Preface
All about COSTs
Growth parameters influence system design
Total Performance Evaluation (TPE)
How to…
1
4
5
3
2

## Slide 3
    Proper prior planning prevents poor performance

## Slide 4
Plan
DO
Check
Action
PDCA

## Slide 5: Type of PFALs
Home appliance
Shop appliance
Research type
Hobby type
Mass production type
  Small scale: Daily harvest 300~500~1000 plants
  Middle scale: Daily harvest 1000~3000~5000 plants
  Large scale: Daily harvest > 5000 plants ~ 50000 plants

## Slide 6: The following contents are more suitable for mass production type of PFALs.

## Slide 7
PFAL related
Mechatronics Tech.
Sensing Tech.
Energy Tech.
Environment Tech.
Disinfection Tech.
Info./commu. Tech.
Bio-Tech.

## Slide 8: To guarantee the success
System: Properly design
HW, SW: Function properly
Quality of Product: Best/Super
Managing: Efficiently
Marketing: Branding, Multi-channel, Multi-product
Finance: Solid, Heathy

## Slide 9
Light
Air
Light
Gas
Water
Nutrient
SD
Product
Environment
Keys/Traps/Opportunities

## Slide 10: Integrated control is needed to function properly
Wind speed at 0.3~1 m/s
Proper leaf and air temperature
Bacteria controlled at least amount
CO2 keep at 1000~2000 ppm
DLI < 14 for leaf lettuce, 17 mol/m2 for Semi-head lettuce
Humidity keep at 70~85% (VPD at proper range)
EC content keep at proper range with little variation
光
氣
濕
溫
風
養
菌

## Slide 11: Outline
Preface
All about COSTs
Growth parameters influence system design
Total Performance Evaluation (TPE)
How to…
1
2
4
5
3

## Slide 12: How to avoid cross contamination?
Big rich
Nutrient
tank
養液槽
養液槽
養液槽
養液槽
栽培床
栽培床
栽培床
栽培床
pH
EC
adjusted
12
RO water
Cultural bed
Nutrient solution tank
Nutrient solution tank
Nutrient solution tank
Nutrient solution tank
Cultural bed
Cultural bed
Cultural bed

## Slide 13: How to operate pump(s) in solution tank?
13
Intermittent type
Continuous type
Required certain flow velocity of the nutrient solution to ensure accuracy of the sensor readout.
Need circulation in the tank to ensure rich in DO and improve uniformity of nutrients.

## Slide 14: What is DLI (Daily Light Integral)? DLI = f(PPFD, L)
PPFD: Photosynthetic Photon Flux Density, in micro-mole per square meter per second
Leafy lettuce
Semi-head lettuce

## Slide 15
DLI = PPFD * L * 3.6 / 1000
PPFD in mol/m2/s
L in hr/day
日累積光量 (DLI)
DLI in mol/m2/day
How to calculate Daily Light Integral (DLI)?
PPFD

## Slide 16
日累積光量 (DLI)
PPFD
Daily Light Integral (DLI)

## Slide 17
DLI
22
20
18
16
14
12
10
8
222
200
177
155
133
111
89
67
45
22
FM

## Slide 18
A.J. Both, 2003

## Slide 19
TLI = DLI * Days
DM = 0.045 * FM
FM = DM / 0.045
100 g FM * 0.045 = 4.5 g DM
35 days
DLI = 8.57 11.42 14.3 17.14 20 22.85
A.J. Both, 2003

## Slide 20
DLI = 11 12 13 14 15 16 17
A.J. Both, 2003

## Slide 21
A growth model was developed based on DLI and CO2 concentration.
A.J. Both, 2003

## Slide 22: How to select the most profitable crops based on Engineering Economic Analysis (EEA)?

## Slide 23: Which crop make the most profit?
 | Crop A | Crop B
Cost, NT$/plt | 20 | 200
Price, NT$/plt | 100 | 1000
Profit, NT$/plt | 80 | 800

## Slide 24
 | Crop A | Crop B
Cost, NT$/plt | 20 | 200
Price, NT$/plt | 100 | 1000
Profit, NT$/plt | 80 | 800
Cropping density, plt/m2 | 25 | 10
Profit per unit area, NT$/m2 | 2000 | 8000
Which crop make the most profit?

## Slide 25: Which crop make the most profit?
 | Crop A | Crop B
Cost, NT$/plt | 20 | 200
Price, NT$/plt | 100 | 1000
Profit, NT$/plt | 80 | 800
Cropping density, plt/m2 | 25 | 10
Profit per unit area, NT$/m2 | 2000 | 8000
Duration, month | 1 | 6
Annual profit per unit area, NT$/m2/yr | 24,000 | 16,000

## Slide 26: Which crop make the most profit?
 | Crop A | Crop B
Cost, NT$/plt | 20 | 200
Price, NT$/plt | 100 | 1000
Profit, NT$/plt | 80 | 800
Cropping density, plt/m2 | 25 | 10
Profit per unit area, NT$/m2 | 2000 | 8000
Duration, month | 1 | 6
Annual profit per unit area, NT$/m2/yr | 24,000 | 16,000
Initial Investment, NT$/m2 | 50,000 | 5,000

## Slide 27: Cash Flow of Crop A & B
 | Crop A | Crop B | A-B | IRR
Year 0 Initial Investment, NT$/m2 | 50000 | 5000 | -45000 | 
Year 1 Annual Net Profit, $/m2/yr | 24,000 | 16,000 | 8000 | -82%
Year 2 | 24,000 | 16,000 | 8000 | -48%
Year 3 | 24,000 | 16,000 | 8000 | -26%
Year 4 | 24,000 | 16,000 | 8000 | -12%
Year 5 | 24,000 | 16,000 | 8000 | -4%
Year 6 | 24,000 | 16,000 | 8000 | +2%
Year 7 | 24,000 | 16,000 | 8000 | +6%
Pay back year: in between 5 to 6 years

## Slide 28: Four rates for beginners
Interest rate
Inflation rate
Return rate (internal rate of return, IRR)
Exchange rate

## Slide 29: How to operate a PFAL to guarantee success?
Survival rate
Sale rate
Two more ‘rates’

## Slide 30: Performance evaluation index: Rate of Sale
Profit = Revenue – Cost
Price 30 NT$/plt，Amount 100 plants，Cost 20 NT$/plant
Rate of Sale 100%，Profit = (30 – 20) * 100 = 1000
Rate of Sale 70%，Profit = (30 – 20) * 100 * 0.7 = 700
30 * 0.7 * 100 - 20 * 100 = 100
30 * 0.7 * 100 - 20 * 100 = 100
?

## Slide 31: Performance evaluation index: survival rate
plant 100 seeds, harvest 70 plants, harvest rate 70/100 = 70%
harvest 100 plants, how many seeds required? 100/0.7 = 142.8 = 143
(130 – 100)/100 = 30%
(130 – 100)/100 = 30%

## Slide 32: Survival rate
Stages
  1. seeding
  2. seedling
  3. mature
All stages have survival rates to consider (SR1, SR2, SR3)
Total survival rate SR = SR1 * SR2 * SR3
  SR = 0.7 * 1.0 * 1.0 = 0.7
  SR = 0.9 * 0.9 * 0.9 = 0.729
Which is better? Why?
high SR is better?

## Slide 33: Survival rate of all stages influencing Cost
SR = SR1 * SR2 * SR3
  Case a: SR = 0.7 * 1.0 * 1.0 = 0.7
  Case b: SR = 0.9 * 0.9 * 0.9 = 0.729
Costs involved with depreciation + labor + utility + materials + marketing + other overhead cost
Assuming totally 100 plants, total cost= 20 NT$/plt (cost in 3 stages are 3, 7, 10, respectively)
Cost = Amount x cost in each stage x accumulative SR of previous stage
  Case a: cost= 100 * (3 * 1 + 7 * 0.7 + 10 * 0.7) = 1490
  Case b: cost= 100 * (3 * 1 + 7 * 0.9 + 10 * 0.81) = 1740

## Slide 34
Successful rate to grow and to sell are both critical

## Slide 35: Sale (marketing) rate and survival rate
Net profit = Quantity x (price x sale rate x SR – sum of (cost of each stage x accumulative SR of previous stage))
Quantity: 100 plants
Cost: 20 NT$/plt (3, 7, 10 for each stage, respectively)
Price: 30 NT$/plt
Sale rate | Survival rate | Net Profit
100% | 100% | 100 * (30 – 20) = 3000 – 2000 = 1000
70% | 100% | 100 * (30 * 0.7 – 20) = 2100 – 2000 = 100
70% | 70% = 0.7 * 1 * 1 | 100 * [30 * 0.7* 0.7 – (3 * 1 + 7 * 0.7 + 10* 0.7)] = 1470 – 1490 = -20
70% | 72.9%= 0.93 | 100 * [30 * 0.7 * 0.729 – (3 * 1 + 7 * 0.9 + 10* 0.81)] = 1531 – 1740 = -209

## Slide 36
When sale rate low, no need to enhance Survival rate (SR high, loss more)
When with same sale rate, SR high does not guarantee high profit. Still need to know SR(i).
SR(i) high in later stages are preferable.
price
price
price
Net profit
Net profit
Net profit
Sale rate
Sale rate
Sale rate
Quantity
Survival rate
Cost
Stage 1 2 3
SR(i)
Cost(i)
Quantity
Survival rate
Cost
Stage 1 2 3
SR(i)
Cost(i)
Quantity
Survival rate
Cost
Stage 1 2 3
SR(i)
Cost(i)

## Slide 37
Loss/elimination should happened as early as possible
price
Net profit
Sale rate
Quantity
Survival rate
Cost
Stage 1 2 3
SR(i)
Cost(i)
price
Net profit
Sale rate
Quantity
Survival rate
Cost
Stage 1 2 3
SR(i)
Cost(i)
price
Net profit
Sale rate
Quantity
Survival rate
Cost
Stage 1 2 3
SR(i)
Cost(i)
Fail in early stage is a blessing to the business

## Slide 38: Performance evaluation index Annual profitability per area
Annual profitability per area
What kind of area:
  Floor area / Production area / Growth area
Example
  A PFAL can have annual net profit of 4 Million NT$
  1000 m2 / 500 m2 (50% for plant production) /2000 m2 (4 tiers)
  Annual profitability per area equals
    4000 NT$/m2 floor area/year
    8000 NT$/m2 production area/year
    2000 NT$/m2 growth area/year
Based on these numbers and expected payback years, one can determine the reasonable amount of investment.

## Slide 39
5 NT$/plt * 25 plt/m2 * 20 = 0.25 x 10k NT$/m2/yr
Expected payback year is 4 years.
The investment should not exceed 2.36 * 4 = 9.44 x 10 k NT$ per meter
10k NT$/m2/yr
100% sale rate and SR
Net profit
NT$/plt
Plt/m2
Plt/m2
Plt/panel
Size of panel m2
Assuming 30 plants per panel was used,
A crop with 20 NT$ per plant of net profit was selected.
Annual production can have 20 batches per year.
Batches per year
Based on growth area

## Slide 40: Outline
Preface
All about COSTs
Growth parameters influence system design
Total Performance Evaluation (TPE)
How to…
1
2
3
4
5

## Slide 41: Costs
Fixed cost
  Thermally insulated envelope Depreciation 10 ~ 20 years
  Supporting and production related facilities Depreciation 3 ~ 5 years
Operating costs
  depreciation
  utility
  labor
  materials
  managing
  Sale
  Misc.
  Rent
  Loan
  Tax
  Etc.

## Slide 42: Fixed (setup) cost
Price on Land (not included)
Price on construction (varied)
For an existing facility (Price on turnkey)
  Based on growth area
  Based on floor area
  Based on daily production, such as
    100 kg/day or 1000 plants/day
  Should includes
    Production related facility: benches, light source, hydroponics system, controls on aero-and root environment, etc.
    Supporting facility: thermally insulated envelope, HVAC, RO water, disinfection system, etc.

## Slide 43: Setup (Fixed) Cost of PFAL in Japan
Company | Floor Area (Growth area) m2 | Tier | Plts/day | Annual yield per area* kg/m2/yr | Total fixed cost ¥ | Fixed cost k¥/plt | Fixed cost k¥/m2
Green Flavor | (66) | 7 | 300 | (166) | 21.78M | 72.6 | 330
OoToya | (160) | 7 | 350 | (80) | 52.80M | 150 | 330
Urban Farm | 546 (400) | 9 | 1200 | 67 (91) | 0.12B | 100 | (300)
Ozu | (500) | 7 | 1500 | (110) | 0.165B | 110 | 330
Mirai | 1000 | 10 | 4000 | 146 | 0.33B | 82.5 | 330
Fairy Angle | 2870 | 10 | 8000 | 102 | 1.5B | 187 | 519
Mirai | 3000 | 10 | 10000 | 122 | 0.99B | 99 | 330
* Assuming 100 g per plant, continuous production throughout the year

## Slide 44
In Japan, setup cost is about 70 (~180) kYuan/plant, equals 28 k NT$/plant, more than two times the cost in Taiwan.
Price： 0.3 NT$/g
Cost per plt
Price per plt
NT$/plt
NT$/plt
Daily prod.
Annual prod.
Plt/day
Kg/day
10k plt/yr
ton/yr
Revenue
10k NT$/yr
10k NT$/yr
Profit
Fresh Weight/plt
Harvest days/yr
10k NT$
Investment
10k NT$/plt
Setup cost
IRR
2year 3year 4year 5year
14 kNT$/plt

## Slide 45
Price 0.3 NT$/g
10 kNT$/plt
11 kNT$/plt
12 kNT$/plt
13 kNT$/plt
15 kNT$/plt
20 kNT$/plt

## Slide 46: If the retail price go higher…
Cost per plt
Price per plt
NT$/plt
NT$/plt
Daily prod.
Annual prod.
Plt/day
Kg/day
10k plt/yr
ton/yr
Revenue
10k NT$/yr
10k NT$/yr
Profit
Fresh Weight/plt
Harvest days/yr
10k NT$
Investment
10k NT$/plt
Setup cost
IRR
2year 3year 4year 5year
Payback year can be shortened,
IRR can be increased.
Price：0.5 NT$/g

## Slide 47
Price：0.5 NT$/g
10 kNT$/plt
15 kNT$/plt
17.5 kNT$/plt
25 kNT$/plt
30 kNT$/plt
40 kNT$/plt

## Slide 48: 0.5 NT$ per gram Very expensive?

## Slide 49: ¥360 for 120 g (1.2 NT$/g) ¥198 for 60 g (1.32 NT$/g)
70 NT$ for 50 g (1.4 NT$/g)
199~249 NT$ for 142 g (1.4~1.75 NT$/g)
Ｒｅｔａｉｌ Ｐｒｉｃｅ ｉｎ ｓｕｐｅｒｍａｒｋｅｔｓ ｏｆ
Ｔａｉｗａｎ， Ｊａｐａｎ ａｎｄ Ｋｏｒｅａ

## Slide 50: TAIPEI, TAIWAN
142 g 315 NT$

## Slide 51: 2011: 199 NT$/142 g
2013: 288 NT$/142 g
2012: 249 NT$/142 g
1.4 NT$/g
1.75NT$/g
2 NT$/g
2014: 315 NT$/142 g
2015 ~ 2022: 288 NT$/142 g
TAIPEI, TAIWAN

## Slide 52: HK
Source | Sale | Product | Price HK$/100 g | NT$/100 g (1:4.167)
HK | 7/11 | 混裝苗菜 (16 HK$/30 g by iVeggie) | 53.3 | 222
US | Wellcome | 各種生菜與混裝苗菜 (盒裝) | 48.9 | 203
HK | FreshMart | 菠菜 (by UF) | 45 | 187
US | Wellcome | 各種生菜與混裝苗菜 (袋裝) | 44.9 | 187
US | CitySuper | 混裝苗菜 (62 HK$/142g) | 43.7 | 182
US | Wellcome | 各種生菜與混裝苗菜 | 34.9 | 141
HK | FreshMart | 奶油、皺葉生菜 (by UF) | 40 | 167
HK | FreshMart | 羅馬、橡葉、綠卷鬚生菜(by UF) | 30 | 125
US | Wellcome | 奶油萵苣 | 27.9 | 112
Aust. | FreshMart | 混裝苗菜 | 21 | 87
Aust. | Wellcome | 各式芽菜 (15.9/125 g) | 12.72 | 53
0.53~2.22 NT$/g

## Slide 53
Electricity21%
Others
11%
Factor | Value
Fresh weight/head | 80 g
Unit price/head | 0.86 USD
Cost/head | 0.76 USD
Daily production | 1,000 kg
% revenue/sales | 11%
% sold | 95%
% sold to supermarket | 70%
% sold to biz use | 30%
Percentages of cost components of a PFAL producing leaf lettuce in Japan (Ijichi, 2018)
Copyright(C) 2018 JPFA All rights reserved.
Chart: 
| 第 1 四半期 | 第 2 四半期 | 第 3 四半期 | 第 4 四半期
売上高 | 27.3 | 22.4 | 18.7 | 5.7 | 5.9 | 2 | 7 | 11
Labor
21%
Electricity
18%
Logistics 5%
Consumables 6%
Seeds 2%
Others 11%
Profit
11%
Costs for advertising, land etc. are excluded.

## Slide 54
Resource element | Resource consumption | Cost (USD/kg)
Electricity | 7 – 8 kWh/kg | 0.85 - 1.2
Labor | 0.10 – 0.13 h/kg | 1.3 - 1.5
Cultivation area | 3 – 4 m2/kg | 1.1 - 1.4
Seeds, CO2, water, fertilizer, substrate, plastic bags, etc. | --------- | 0.85 - 1.2
Production cost (USD/kg) |  | 4.1 - 5.3
Cost for sales promotion is excluded. One Euro = 130 Japanese yen as of 2017 (redrawn from Kozai, 2018). Labor cost = about 1200 yen/h for part-time workers, about 500,000 yen/month for regular employees as of 2017.
Resource consumption and production cost/kg of leaf lettuce by components in selected PFALs in Japan (Kozai, 2018)
150,000 yen/month in Taiwan
785 yen/h in Taiwan

## Slide 55: More index for performance evaluation
Area required per unit Yield
  How many sq. meters needed to produce 1 kg of vegetable?
Labor required per unit yield
  How many man-hour required to produce 1 kg of vegetable?
Resource required per unit yield
  How many degree of electricity required to …?
  How many Liter of water required to …?
  How many gram of fertilizer required to …?
3 ~ 4 m2/kg
0.10 – 0.13 h/kg
7 – 8 kWh/kg

## Slide 56: Expected cost reduction and sales increase
Initial investment by 30%
Labor cost by 30%
Electricity cost by 30%
Increase in sales per m2 of cultivation space
Annual productivity by 40%
Unit economic value by 15%
Relative CP = (1.40 x 1.15)/(0.70 x (0.26 + 0.21 + 0.18) + 0.35) = 1.61/0.805 = 2.00
Reduction in cost per kg of produce

## Slide 57: LED vs. T5
Cost: 20 NT$/plt
Elec.
Labor
Depreciation
Nutrient
CO2
material
Nutrient
CO2
material
Elec.
Labor
Depreciation
Elec.fee /plt
T5 fluorescent lamp
LED lamp

## Slide 58: LED vs. T5
Cost: 20 NT$/plt
Light source
AC (COP=4)
Fan
Air blower
Water pump
Light source
AC (COP=4)
Fan
Air blower
Water pump
CO2
Seeds
Sponge
Nutrient
Water
Dep.HW.10 yrs
Dep.LED.5 yrs
Labor
CO2
Seeds
Sponge
Nutrient
Water
Dep.HW.10 yrs
Dep.T5.2 yrs
Labor
Sum
Harvest FW
Cost per 100 g
NT$/100 g
Sum
Harvest FW
Cost per 100 g
NT$/100 g
Elec.
Gas
Materials
Nutrients
Depreciation
Labor
Elec.
Gas
Materials
Nutrients
Depreciation
Labor

## Slide 59: More details
Plant distance, cm
density, plts/m2
A
Plts/panel B
C
W L, cm
Stage
1
2
3
Days distance density
Target,plts
Panels needed
tiers
Seeding bench
Seedling bench
Production bench
Plts/panel
ratio
Production
Elimination rate

## Slide 60: Amount of Investment at various size of the PFAL operation and per plant basis unit cost
Plt/day
10k/plt
Daily production
Investment
Growth area needed
It takes 28~32k NT$/plt in Japan
What is the proper size to start with?
How good can you sell your product and at what price ?

## Slide 61
Payback Yr
IRR
Plts/m2
NT$/plt
days
density
Net profit per plant
Cultural period
Net Profit
10k NT$/m2/year
NT$/m2/month
10k NT$
/plt /m2
Investment
Performance evaluation index Pay back year & Internal Rate of Return (IRR)

## Slide 62: Various Net Profit, in NT$/plt
Net profit, in NT$/plant
Pay back Yr
IRR
10k NT$
/plt /m2
10k NT$
/plt /m2
Net profit, in NT$/plant

## Slide 63: Estimation of Space required
Days in Mature stage
Daily harvested
No. of Tiers
Plant distance
Plts/day
days
layers
Total num. of plts
density
Plts/
Total production area
Total bench area
Total area
Other supporting area
ping

## Slide 64: 40 ft cargo container type PFAL
Area
plts
Plts/day
Total plts
Daily harvested
Space utilization
Cultural days
Plant distance, cm
Price of lamp, NT$
Lamp distance, cm
No. lamps
Length.lamp
cm
Cost of lamps
X 10k NT$
Width, m
Length, m
ft
CONTAINER
tiers
Total prod. area
Area/plt
density
m2/plt
Plt/m2
Net profit, 10k
Ratio of Net profit
Revenue, 10k
Retail price, NT$/g
FW, g/plt
Days with harvest
Total plts harvested/yr

## Slide 65: Cost for a 40 ft. cargo container type PFAL
In Japan, 130~200 k NT$/m2
HW besides light source
Light source
Cost
Cost/

## Slide 66: Annual depreciation per plant
sum= 5.65
HW besides light source
Light source
Cost
Cost/
HW besides light source
Light source
Years
NT$/yr
NT$/m2/yr
NT$/plt/yr
Annual depreciation

## Slide 67: Fine tune on key parameters to reduce depreciation
2.01
6.37
sum= 5.65
Depreciation on HW besides light source
NT$/plt/yr
NT$/plt/yr
Depreciation on light source
Space
utilization
Plant
distance
Cultural days
No. of
tiers
Lamp
distance

## Slide 68: Some thought regarding the Operating cost
Light period changed from 12 hr. to 24 hr.
  Operating cost will increased to 2 times (200%)?
  Wrong, only the elec. Cost on lighting will increase.
If the yield just increase 50%, thus, the revenue increase by 50%.
Does it worthwhile to make the change?
Why?

## Slide 69
OP cost per plant
Hrs for light period
Ratio of elec.fee vs. OP cost
Elec.fee
NT$/plt
Other.fee
NT$/plt
Extra Elec.Fee
NEW
OP cost
NEW/OLD
OP cost
NT$/plt
NEW yield/OLD yield
The proper change
For those c/q < 1 (q > c)
are proper changes
Ratio of elec.fee vs. OP cost
NEW/OLD OP cost
NEW/OLD hrs of light period

## Slide 70
c
q
For those c/q < 1 (q > c) are proper changes
Ratio of yield after vs. before
Ratio of OP cost
after vs. before

## Slide 71
操作成本增加倍率
Light period increase from 12 hrs to 24 hrs
Ratio of yield after vs. before
Ratio of OP cost
after vs. before
c/q
c
q

## Slide 72: Outline
Preface
All about COSTs
Growth parameters affect system design
Total Performance Evaluation (TPE)
How to…
1
2
3
5
4

## Slide 73: Growth parameters influence system design
Relative growth rate
Moisture content  quality
Plant size  plant distance
Plant height  lamp2plant distance
Surface temperature of lamp  lamp2plant distance
Plant fresh weight  days of harvest, DLI, PPFD, Photoperiod

## Slide 74
A.J. Both, 2003
growth curves

## Slide 75
Relative growth rate
The slope is the growth rate (r)
Harvest shoot fresh mass, in g/plant | M | 100 | 120 | 60
Shoot FM at transplanting | Mo | 2 | 3.69 | 1
 | Ln(M/Mo) | 3.912 | 3.482 | 4.094
Days from transplanting | t | 21 | 14 | 21
Growth rate | r=Ln(M/Mo) / t | 0.186 | 0.249 | 0.195
21 days：18 batch/yr
14 days：26 batches, 8 more batches
yield increased by 44 %

## Slide 76
Similar pattern for cooling time estimation
Average product temperature during cooling follows a pattern similar to this Figure.
Product is usually finished cooling at 7/8 or 15/16 cool.
As shown in the Figure, this product takes 9 or 12 hours to reach 7/8 or 15/16 cool.
For hydrocooling, generally finished at ½ cool.
For forced air cooling, finished at 7/8 cool.
Tm: temperature of cooling medium
Ti: initial Temperature of the product
T: T of the product at a given time
C: cooling coefficient (the Slope)
θ: the time elapsed (the X)

## Slide 77
Shoot Fresh Weight
Shoot Dry Weight
Root Fresh Weight
Root Dry Weight

## Slide 78: Roots
Plants need the root to grow well.
Growers do not want the root to grow too well.
Roots block the flow, influence the distribution of the nutrients to the roots.
Roots is normally discarded after harvest.
Size of roots should be minimized.

## Slide 79: MC (moisture content)= 1 - DWR
DWR = Dry weight / Wet weight
= Dry weight / (Dry weight + Water)
Days After Transplanting
Moisture content

## Slide 80: Plant height, cm
Days After Transplanting

## Slide 81: Lamp2plant distance can be adjust automatically or manually
PPFD  1/(lamp2plant distance)2

## Slide 82: Leave length, cm
Days After Transplanting
Romaine
Green Oak
Boston
Frilly

## Slide 83: Leave width, cm
Days After Transplanting
Romaine
Green Oak
Boston
Frilly

## Slide 84: L x W x H (in cm)
 | Day 9 | Day 14 | Day 28 | Day 35
Green Oak | 1.7x1.3x0.8 | 6.5x4x3 | 22x21x10 | 27x25x22
Boston | 1.9x1.1x1.3 | 5x2.9x3 | 19x18x9 | 21x20x12
Romaine | 2x1x1.5 | 6.5x2.6x4 | 19x18x11 | 25x22x17
Frilly | 1.8x1.2x1 | 5x4x4 | 17x13x12 | 25x22x18

## Slide 85: Plant distance vs. cropping density
B = 10000 / A2
    example： 69 = 10000 / (122)
C = 100 / sqrt(D)
  example： 2 = 100 / sqrt(2500)
A
C
B
D
Plant distance, cm
Cropping density, plt/m2

## Slide 86: Spacing: operation to change the plant distance
16 plt/tray = 44 plt/m2
144 plt/tray = 400 plt/m2

## Slide 87: Adjustable spacing
harvest
seeding
Nursing
Seedling production
transplanting

## Slide 88: Cultural stage: example
Seedling
Stage 1 (14 days)
Quality Adjustment
Stage 3 (7 days)
Mature
Stage 2 (14 days)
333 plants/m2
40 plants/m2
20 plants/m2

## Slide 89: Cultural Stage: example
Seeding
Stage 1 (7 days)
Mature
Stage 3 (14 days)
Seedling
Stage 2 (14 days)
Density: 333 plants/m2
Density:40 plants/m2
Density: 20 plants/m2

## Slide 90: Environmental settings: example
Parameters | Seedling | Mature | Quality Adjustment
 | Stage 1 | Stage 2 | Stage 3
PPFD (μmol/m2/s) | 230±30 | 270±30 | 
Photo period (L/D ，hr) | 24/0 | 16/8 | 
DLI (mol/m2/day) | 20 | 16 | 
Temperature (L/D ，℃) | 22/20 |  | 
RH度 (%) | 80 ~ 90 |  | 
EC (mS/cm) | 1.2±0.1 |  | 
pH | 5.8±0.1 |  | 
CO2 (ppm) | 1200±100 |  | 

## Slide 91: Cultural stages can be varied due to different conditions
* RUI: Resource Utilization Index
1 stage | 18.9 | 28 | 5 | 3.434 | 0.291 | 0.65

## Slide 92: Automatic spacing in 1 dimension

## Slide 98: Automatic spacing in 2 dimensions
Upot

## Slide 99: Air change per hour (ACH) air change per minute (ACM)
Simplified terms to describe the ventilation rate of a confined environment such as tissue culture vessel, naturally or forced ventilated greenhouse and plant factory with artificial lighting.

## Slide 100
There are no plants and no workers in the PFAL/NVGH/TC. Vessel
Enrich CO2 to the indoor to reach high concentration
NVGH: 3~4000 ppm
PFAL: 8000 ppm
Tissue Culture Vessel (T.C. vessel): 10000 ppm
This is C0
Allow the CO2 concentration to drop naturally.
Measuring the indoor CO2 concentration in real time if possible
NVGH, PFAL, real time measurement is preferred
T.C. vessel: 30 min to 1 hour interval
Track the Time and the CO2 concentration for at least 2 points (T1, C1; T2,C2)
with at least one hour interval
Steps to measure ACH

## Slide 101
Measuring ACH
N=ln((C1-C0)/(C2-C0))/T
Where,
ln: natural log
T=T2 - T1 (h)
Time is the X axis,
Natural log of CO2 concentration difference at Ti minus Co
N is the slope
T1=2, T2=3
C0=360, C1=10000, C2=4000 (ppm)
→N=ln(9640/3640)/(3-2) = 0.97/h
T2
T1

## Slide 102: net photosynthesis rate involving ACM or ACH

## Slide 103
Net Photosynthesis rate (Pn) of PFAL/NVGH
Pn=k·n·v·(Co-Ci)
Where,
Pn: in ml/h·GH or PFAL
k: conversion factor from ml to g (1.96 x 10-6)
n: ACH
v: volume of the GH or PFAL
Co , Ci : CO2 concentration of outdoor and indoor, ppm
Pn per unit dry mass = Pn/dry mass growth in GH PFAL
By adjusting light intensity, temperature and indoor CO2 to grow plants, after harvested, dry mass can be measured and Pn per unit dry mass under various conditions can be derived.
Notes: 單位培養器皿的淨光合作用速率 Pv (ml/h·vessel) 可由下式求得 :
Pv=k·N·V·(Co-Ci)
這裡的 k 是將二氧化碳從容積 (ml) 轉換為質量 (g) 的變換係數 (1.96 x 10-6g)；
N 是換氣率；V 是培養器皿的容積。
Co 和 Ci 的單位是 ppm，準確來說是 µmol/mol 。
此外 N 和 V 的積為培養器皿內單位時間的換氣量。
Co 和 Ci 的差變小的同時 Pv 的計算誤差會變大。
單位培養植物、單位葉面積以及單位乾重的淨光合作用速率可將 Pv 分別除以單位培養器皿的培養植物數、葉面積以及乾重去求得，
此時可改變光強度、溫度或測量是內的二氧化碳濃度去進行各式各樣的 Pv 計算。

## Slide 104
Net Pn of Forced Ventilated GH
Air at flow rate (in ml/h or m3/h) is forced to pass through the FVGH
Plant will consumed CO2, thus CO2 of incoming outdoor air (Co) will be higher than CO2 of the outgoing indoor air (Ci)
When Ci maintain at steady state, the Pn of the indoor plants can be calculated as follows:
Pn=k··(Co-Ci)
Notes: 還有另一種方法可以算 Pv，
就是把培養植物的一部分、全部，甚至是複數株培養植物放在測量室內，
然後把已知流量 v (ml/h) 的空氣以幫浦強制輸送。
測量室內培養植物的光合作用把二氧化碳消耗掉之後，出口空氣的二氧化碳濃度 Co 就會比入口空氣的 Ci 還低。
當 Co 的值幾乎不隨時間變動時，測量室內的培養植物 Pv 就能用以下式子算出 :
Pv=k·v·(Co-Ci)
這裡的 k 是前面提及的變換係數，v 是空氣流量 (ml/h)，由於 v 會和上式的 N, V 乘積相等，所以兩個式子是一樣的。若空氣流量比培養植物的大小、株數、光強度等等還大很多的話 (Co-Ci) 的值就會變小，進而提高計算誤差。另外，測量室的容積要室過大就會導致 Co 的安定所需時間變長。

## Slide 105: mass balance involving ACH

## Slide 106
Without CO2 enrichment
Without CO2 enrichment
Air Change per Hour of a NVGH
The setpoint should be at 400 vpm, if CO2 enrichment is installed
400 vpm
ACH=20
ACH=3
Naturally Ventilated Greenhouse (NVGH)
EX1

## Slide 107
 | ACH | CO2.in | Value Shown in Fig. | Calculated Value CO2 going into GH | 
GH without CO2 enrichment | 20 | 380 ppm | 45 | 43.01 | 47.48
GH without CO2 enrichment | 3 | 290 | 40 | 35.49 | 39.18
Assuming CO2 density 1.18, ppm to mg/kg is 1.519
Assuming CO2 density 1.29, ppm to mg/kg is 1.534
Greenhouse (GH) is 6 m height, floor area is 1 ha
Air flow rate (A) = ACH * 6 * 10^4 * 1.18 (m3/h * kg/m3) in kg air/ha/h
CO2 difference (B) = (CO2.in-400) * 1.519 in mg CO2/kg air
Rate of CO2 going into the GH (C) = A*B /10^6, in mg CO2/ha/h
ACH=20, CO2.in=380 ppm, C=20*6*10^4*1.18*(380-400)*1.519/10^6 = -43.01
ACH= 3, CO2.in=290 ppm, C= 3*6*10^4*1.18*(290-400)*1.519/10^6 = -35.49
ACH=20, CO2.in=380 ppm, C=20*6*10^4*1.29*(380-400)*1.534/10^6 = -47.49
ACH= 3, CO2.in=290 ppm, C= 3*6*10^4*1.29*(290-400)*1.534/10^6 = -39.18
Assuming CO2 density 1.18, ppm to mg/kg is 1.519
Assuming CO2 density 1.29, ppm to mg/kg is 1.534
Calculated values are different from values shown in the figures are mainly due to two constants used.
Fundamentals of Plant Factory with Artificial Lighting (PFAL) By: Wei Fang, Ph.D., Professor, NTU_BME)

## Slide 108
With CO2 enrichment
With CO2 enrichment
In a CO2 enriched NVGH
The ACH should be as small as possible
400 vpm
ACH=20, 73.3% of CO2 is wasted
ACH=3, 69.4% of CO2 is wasted
EX2

## Slide 109
 | ACH | CO2.in | Value Shown in Fig. | Calculated Value CO2 going out of GH | 
GH With CO2 enrichment | 20 | 450 | 132 | 107.54 | 118.7
GH With CO2 enrichment | 3 | 750 | 125 | 112.9 | 124.6
Assuming CO2 density 1.18, ppm to mg/kg is 1.519
Assuming CO2 density 1.29, ppm to mg/kg is 1.534
Greenhouse (GH) is 6 m height, floor area is 1 ha
Air flow rate (A) = ACH * 6 * 10^4 * 1.18 (m3/h * kg/m3) in kg air/ha/h
CO2 difference (B) = (CO2.in-400) * 1.519 in mg CO2/kg air
Rate of CO2 going out of the GH (C) = A*B/10^6, in mg CO2/ha/h
ACH=20, CO2.in=450 ppm, C=20*6*10^4*1.18*(450-400)*1.519/10^6 = 107.54
ACH= 3, CO2.in=750 ppm, C= 3*6*10^4*1.18*(750-400)*1.519/10^6 = 112.9
ACH=20, CO2.in=450 ppm, C=20*6*10^4*1.29*(450-400)*1.534/10^6 = 118.7
ACH= 3, CO2.in=750 ppm, C= 3*6*10^4*1.29*(750-400)*1.534/10^6 = 124.6
Calculated values are different from values shown in the figures are mainly due to two constants used.

## Slide 110
A greenhouse has a volume of 3000 m3, ACH is 0.75. Indoor air T is 20 oC, RH is 70 %, outdoor CO2 is 345 ppm. Indoor CO2 keep at 1000 ppm (1519 mg/kg) to promote plant growth. What is the loss rate of CO2 ? Assuming 20 NT$ per kg CO2, what is the loss per day? What if indoor CO2 changes to 380 ppm?
Sol: T=20 oC, RH=70 %, air density=1.18 kg/m3
mair = 1.18 kg/m3 * 3000 * 0.75 /3600 = 0.7375 kg/s
mvo = 0.7375 kg/s * 1.519 * (1000 – 345) mg/kg = 733.8 mg/s = 2.64 kg/hr
Loss per day = 2.64 * 24 * 20 = 1267 NT$
Loss = 1267 * (380-345)/(1000-345) = 67.7 NT$
EX3

## Slide 111
A PFAL has a volume of 3000 m3, ACH is 0.75. Indoor air T is 20 oC, RH is 70 %, outdoor CO2 is 345 ppm. Indoor CO2 keep at 1000 ppm (1519 mg/kg) to promote plant growth. What is the loss rate of CO2 ? Assuming 20 NT$ per kg CO2, what is the loss per day? What if ACH changes to 0.01?
Sol: T=20 oC, RH=70 %, air density=1.18 kg/m3
mair = 1.18 kg/m3 * 3000 * 0.75 /3600 = 0.7375 kg/s
mvo = 0.7375 kg/s * 1.519 * (1000 – 345) mg/kg = 733.8 mg/s = 2.64 kg/hr
Loss per day = 2.64 * 24 * 20 = 1267 NT$
Loss = 1267 * 0.01/0.75 = 16.89 NT$
EX4

## Slide 112
Carbon Dioxide produced By Animals
Rule of thumb: Every 24.6 kJ of total heat added to the environment by an animal will produced 1 L of CO2. (1 L/s CO2 = 24.6 kW)
CO2 concentration outdoor is 345 ppm (parts per million, vpm), 345 x 1.519 = 524 mg of CO2/kg of Air.
Given the flow rate of the animal house is 4.3 m3/s, the total amount of heat produced by the animals is 361.8 kW.
CO2 produced (Vp) = 361.8 / 24.6 = 14.7 L/s = 0.0147 m3/s
Vp + Vvi = Vvo
0.0147 + [4.3 m3/s * 0.000345 ] = [4.3 m3/s * CO2indoor]
CO2indoor = 0.003764 = 3764 ppm
EX5

## Slide 113
Mass balance of CO2 enrichment
CO2outdoor= 350 ppm = 686 mg/10^6 m3
CO2supply=0~1000 mg/h=0~22.72 mmolCO2/h
Volume=20~100 m3
Tindoor=25 C
ACH=0.1
CO2indoor can be calculated
Cleak can be calculated
Csupply = Cassimilated+Cleak
mmolCO2 h-1
mgCO2 h-1
m3
Your Homework to redraw this figure
EX6

## Slide 114
Water /CO2 utilization can be calculated based on mass balance and ACH.

## Slide 115: Outline
Preface
All about COSTs
Growth parameters influence system design
Total Performance Evaluation (TPE)
How to…
1
2
3
4

## Slide 116: Total Performance Evaluation (TPE) for PFAL design and operation
Based on Quantitative index
How to select the crop?
How to choose the most suitable lamps?
How to operate a PFAL to guarantee success?

## Slide 117: The 1st Quantitative index
Photons vs. Energy consumption
QE ratio = PPFD x Area / energy consumed by the light source (in μmol/J)

## Slide 118: How to choose the light source?
b
a
c
d
a x b / (c x d)
= mol/J
PPFD
Area
No. lamps
Power/lamp
QE ratio
Relative
QE ratio
QE ratio: Quantum generated vs. Energy consumed by the light source

## Slide 119: Two definitions on mol/J
Light beam vs. its own energy
  E = h * C / 
Light beam vs. Energy of the electricity input
It is termed ‘QE ratio’

## Slide 120
Conversion factor from energy to quantum and vise versa

## Slide 121: E: energy h: Planck constant C: speed of light : wavelength

## Slide 122
This is another μmol/J
E=
Number of photons under same amount of energy
Energy of 1 mol of photos at various wavelength

## Slide 123: Two definitions on mol/J
Light beam vs. its own energy
  E = h * C / 
Light beam vs. Energy of the electricity input
It is termed ‘QE ratio’
It is an index for lighting efficacy
An index for the arrangement, installation and selection of light source

## Slide 124
Lighting efficacy, in μmol/J, is the index to evaluate the selection and installation of lamps on top of a cultural bed
  PPFD (in μmol m-2 s-1) need to measured at a fixed distance for comparison (say FL: 20 cm, LED: 10 cm)
Cultural bed
Distance (cm)
n
p
L
A
QE ratio = L*A/(n*P)
μmol/J

## Slide 125
Too far away from light to plant
QE ratio

## Slide 126: T5 FLs at 10 cm interval
T5 FLs at 20 cm interval w/ reflector

## Slide 127: Reflectors make a great difference in improving the QE ratio
Arrangement | QE ratio mol/J
 | 1.0
 | 1.2
 | 1.3
 | 1.6
 | 1.8

## Slide 128
With reflector
PPF increase from 113 to 229 mol/m2/s
Cold Cathode Fluorescent Lamp
Efficiency of light source is too low

## Slide 129
LED | reflector | Distance below lamps (cm) | Avg. PPFD ( μmol m-2 s-1 ) | Area ( m2 ) | PPFD x Area ( μmol s-1 ) | Power ( W ) | QE ratio ( μmol J-1 )
9 CW LED | no | 10 | 199.6 ± 43.8 | 2.16 | 431.1 | 189 | 2.3
9 CW LED | yes | 10 | 273.9 ± 79.8 | 2.16 | 589.7 | 189 | 3.1
w/o reflector
w/ reflector
Impact of reflectors on QE ratio

## Slide 130
Totally 6 lamps, turn on only 2 lamps at both edges.
Adjust the orientation of these 2 by 0, 20, 40 degree toward cultural bed.
Turn 40 degree toward cultural bed is the best.
40o
0o
20o
0o
20o
40o
Impact of rotating angle of 2 lamps at the edge of the cultural bed on Le

## Slide 131
40 度
Turn on all 6 lamps
Adjust 2 lamps at the edge at 0, 20, 40 degree toward cultural bed.
0
20
40
60
80
100
120
140
160
180
0
20
40
60
80
100
120
40o
0o
0o
40o
20o
20o
Avg. PPFD
313
326 
334


## Slide 132
Corp. and tube length of CW LEDs | Distance under lamp (cm) | PPFD (μmol m-2 s-1) | Area (m2) | PPFD x Area (μmol/s) | Power per tube (W/tube) | No. tubes | Total Power (W) | QE ratio μmol/J
SA_CW_1.8 m (0 deg.) | 10 | 313.6 ± 69.8 | 2.16 | 677.5 | 28.83 | 6 | 172.97 | 3.9
SA_CW_1.8 m (20 deg.) | 10 | 326.2 ± 77.4 | 2.16 | 704.6 | 28.83 | 6 | 172.97 | 4.1
SA_CW_1.8 m (40 deg.) | 10 | 334.9 ± 86.6 | 2.16 | 723.4 | 28.83 | 6 | 172.97 | 4.2
AR_CW_1.2 m (0 deg.) | 10 | 281.6 ± 59.4 | 2.16 | 608.4 | 21.67 | 9 | 195.00 | 3.1
Save 11.8 %
improve 18.9 %
improve 35.5 %
QE ratioof various Lamps installed per cultural bed
*Area of cultural bed：1.2 m x 1.8 m

## Slide 133: Lighting efficiency (QE Ratio)
Comp_Spec of Light sources | Reflectors on top | No. of tubes or panels | PPF* μmol m-2 s-1 | PPF x Area ( μmol s-1 ) | Power consumption, W | QE ratio μmol J-1
S_CW1.8 | Y | 6 Tubes | 334.9 ± 86.6 | 723.4 | 172.97 | 4.2
T_V | Y | 9 tubes | 281.6 ± 59.4 | 608.4 | 195 | 3.1
H_CW | Y | 9 tubes | 273.9 ± 79.8 | 73.9 | 212 | 3.1
T_A | Y | 9 tubes | 225.8 ± 49.1 | 487.8 | 189 | 2.6
E_CW | Y | 9 tubes | 263.8 ± 64.2 | 569.8 | 228 | 2.5
T_A | no need | 12 panels | 411.5 ± 103.2 | 888.9 | 432 | 2.1
T_N | Y | 9 tubes | 186.7 ± 39.3 | 403.2 | 196 | 2.1
E_WW | Y | 9 tubes | 210.8 ± 51.0 | 455.3 | 229 | 2.0
T_N | no need | 12 panels | 378.4 ± 95.4 | 809.6 | 428 | 1.9
T_M | Y | 9 tubes | 168.0 ± 39.1 | 326.9 | 193 | 1.9
T_M | no need | 12 panels | 387.3 ± 99.4 | 836.5 | 442 | 1.9
T_Y | Y | 9 tubes | 168.3 ± 34.7 | 363.5 | 188 | 1.9
S_R | no need | 12 panels | 291.0 ± 71.3 | 628.6 | 334 | 1.9
T5FL_CW | Y | 9 tubes | 250.0 ± 57.5 | 540 | 283 | 1.9
* Measured at 10 cm distance under light except the T5FL treatment (at 20 cm distance)
** Area of culture Bed on bench per layer = 1.8 m x 1.2 m = 2.16 m2

## Slide 134: Quantitative measures
Knowing µmol / J (QE ratio) is not enough
We defined two new terms
    PY (photon yield): gFW/mole of photons provided from seeding (sowing) to harvest
    EY (energy yield): gFW/degree of energy consumed from seeding (sowing) to harvest

## Slide 135: 4 types of LED panel, 2 types of lettuce

## Slide 136: Which crop make better use of light?
 | Lettuce 1 |  | Lettuce 2 |  | Overall QE ratio | 
 | PY g/mole | EY g/deg. | PY g/mole | EY g/deg. | mole/deg. | ratio
LED1 | 32.2 | 44.2 | 18.5 | 25.3 | 1.4 | 1
LED2 | 31.1 | 101.2 | 22.0 | 71.6 | 3.3 | 2.35
LED3 | 34.4 | 67.0 | 20.7 | 40.4 | 1.9 | 1.35
LED4 | 32.0 | 74.8 | 20.1 | 46.9 | 2.3 | 1.64
Avg. | 32 | 72 | 20 | 46 |  | 
Lettuce 1 generate 60% more biomass under same amount of light. (g/mol)
Lettuce 1 generate 56% more biomass under same power consumption. (g/deg)

## Slide 137: Which LED is the best for the crop?
 | Lettuce 1 |  | Lettuce 2 |  | Overall QE ratio | 
 | PY g/mole | EY g/deg. | PY g/mole | EY g/deg. | mole/deg. | ratio
LED1 | 32.2 | 44.2 | 18.5 | 25.3 | 1.4 | 1
LED2 | 31.1 | 101.2 | 22.0 | 71.6 | 3.3 | 2.35
LED3 | 34.4 | 67.0 | 20.7 | 40.4 | 1.9 | 1.35
LED4 | 32.0 | 74.8 | 20.1 | 46.9 | 2.3 | 1.64
Avg. | 32 | 72 | 20 | 46 |  | 
biomass production per power consumption: LED2 > LED4 > LED3 > LED1 for both lettuce (can be seen under DY and mol/deg)

## Slide 138: Which crop to select?
E = A*B*C*D /1000
G = E / F
1 kW.hr = 1 Degree
35 days
Stages
1
2
3
Romaine
Green Oak
Frilly
g/plant
deg/plt
g/deg

## Slide 139: Strong light condition (z1)
D = B*C*3.6 /1000
F = D*E / A
PPFD, in mol/m2/s
DLI, in mol/m2/day
PPFD
mol/plt
Stages
1
2
3
Plt/m2

## Slide 140: The 2nd Quantitative index
PY = FW/TLI (in g/mol)
  Photon Yield: One mole of photon can produce how many grams of plants
  FW: Fresh weight per plant, in g/plant
  TLI: overall Total Light Integral per plant, in mol/plant

## Slide 141: TLI: overall total light integral
DLI = PPFD x hrs x 3.6 / 1000
PPFD in mol/m2/s
Hrs: light period per day
DLI in mol/m2/day
TLI : overall Total Light Integral per plant
s | A | B | C | TLI(s)=B*C/A
 | plt/m2 | DLI | days | mol/plt
1 | 333 | 20 | 14 | 0.84
2 | 40 | 16 | 14 | 5.6
3 | 20 | 17 | 7 | 5.95
 |  |  | Sum | 12.39

## Slide 142: The 3rd quantitative index
D = C / B, values should be the same among treatments
Romaine
Green Oak
Frilly
g/plant
g/mol
g/deg
mol/deg
Energy Yield: EY (g/degree)
PY
EY

## Slide 143: Low light condition (z2)
Stages
1
2
3
Romaine
Green Oak
Frilly
g/plant
g/deg
mol/deg
mol/plt
Plt/m2
PPFD

## Slide 144: z1 vs. z2
In low light condition (z2)
  g/mol (PY) is higher
In strong light condition (z1)
  g/plt is higher
  g/degree (EY) is higher
  mol/degree is higher

## Slide 145: Code N??_E??_F??_D?? N??_E??_L??_??_D??
N ? | E ? | F ? L ??_?? | D ?
Type of nutrient solution (NS) formula | Concentration of NS by EC in mS/cm, or dS/m. | Type of artificial light F: Fluorescent lamp L: LED And PPFD value in mol/m2/s | DLI in mol/m2/day
N1, N2 | E1.2 E0.1, E0.6, E1.2 | F 230, 270 L 9R 100 L 8R1B 100 L 4CW4R1B 100 L 9CW 100 L RB 270 | D 16 D 20, 16, 9 D 15, 16, 17, 18

## Slide 146: DLI in mol/m2/day
DLI =PPFD x Light period (hr/day) x 3.6 / 1000
PPFD | 230 mol/m2/s | 270
Light period | 24 hrs | 16 hrs
DLI | 230 x 24 x 3.6 / 1000 = 19.87 | 270 x 16 x 3.6 / 1000 = 15.55

## Slide 147: 1. Variation on Nutrient
treatment | Stage 1 (1~14 days) | Stage 2 (15~28 days) | Stage 3 (29~35 days)
1 | N1_E1.2_F230_D20 | N1_E1.2_F270_D16 | N1_E1.2_F270_D16
2 |  | Same with above | N1_E0.6_F270_D16
3 |  | Same with above | N2_E1.2_F270_D16
4 |  | Same with above | N3_E0.1_F270_D16
5 |  | Same with above | N3_E0.1_F270_D16*
6 |  | N2_E1.2_F270_D16 | N2_E1.2_F270_D16
7 |  | Same with above | N2_E0.6_F270_D16
N1：迦南農場配方，N2：花寶1號，N3：清水
E：EC, in mS/cm
F：Color Temperature 3000 K, Fluorescent lamp, in μmol/m2/s
D：DLI in mol/m2/day
*：treated for only 3 days prior to harvest (DAS 33~35, others treated for 7 days

## Slide 148: 2. Variation on Light quality
treatments | Stage 1 (1~14 days) | Stage 2 (15~28 days) | Stage 3 (29~35 days)
8 | N1_E1.2_F230_D20 | N1_E1.2_F270_D16 | N1_E1.2_L9R_100_D9
9 | Same with above | Same with above | N1_E1.2_L8R1B_100_D9
10 | Same with above | Same with above | N1_E1.2_L4CW4R1B_100_D9
11 | Same with above | Same with above | N1_E1.2_L9CW_100_D9
E：EC, in mS/cm
L：LED, 9R: totally red, 9 red chips in one unit of light source
8R1B: 8 red chips 1 blue chips in one unit,
4CW4R1B: 4 CW chips, 4 red chips and 1 blue chip per unit,
9CW: 9 CW chips per unit of light source, all in μmol/m2/s
D：DLI in mol/m2/day

## Slide 149: 3. Variation on DLI＠stage 3 only
Fluorescent lamp: three wavelength T5, Color temperature 3OOO K (Wellpower, Taiwan)
treatments | Stage 1 (1~14 days) | Stage 2 (15~28 days) | Stage 3 (29~35 days)
12 | N1_E1.2_F230_D20 | N1_E1.2_F270_D16 | N1_E1.2_F270_D15
13 | Same with above | Same with above | N1_E1.2_F270_D16
14 | Same with above | Same with above | N1_E1.2_F270_D17
15 | Same with above | Same with above | N1_E1.2_F270_D18

## Slide 150: 4. Variation on nutrient under fixed DLI
treatments | Stage 1 (1~14 days) | Stage 2 (15~28 days) | Stage 3 (29~35 days)
16 | N1_E1.2_F230_D20 | N1_E1.2_F270_D16 | N1_E0.6_F270_D17
17 |  | Same with above | N2_E1.2_F270_D17
18 |  | N2_E1.2_F270_D16 | Same with above
19 |  | Same with above | N2_E0.6_F270_D17

## Slide 151: 5. Using RB LED under fixed DLI
treatments | Stage 1 (1~14 days) | Stage 2 (15~28 days) | Stage 3 (29~35 days)
20 | N1_E1.2_F230_D20 | N1_E1.2_F270_D16 | N1_E0.6_LRB_270_D17
21 | Same with above | Same with above | N1_E0.2_LRB_270_D17

## Slide 152: ＰY
Treat-ments | Stage 1 (Day 1~14) | Stage 2 (Day 15~28) | Stage 3 (Day 29~35) | Total LI | Shoot FW | ＰY
1 | N1_E1.2_F230_D20 | N1_E1.2_F270_D16 | N1_E1.2_F270_D16 | 12.04 | 138.86 | 11.52
2 |  |  | N1_E0.6_F270_D16 |  | 106.50 | 
3 |  |  | N2_E1.2_F270_D16 |  | 125.68 | 
4 |  |  | N3_E0.1_F270_D16 |  | 79.89 | 6.63
5 |  |  | N3_E0.1_F270_D16* |  | 109.55 | 
6 |  | N2_E1.2_F270_D16 | N2_E1.2_F270_D16 |  | 91.89 | 
7 |  |  | N2_E0.6_F270_D16 |  | 85.16 | 

## Slide 153
Treat-ments | Stage 1 (Day 1~14) | Stage 2 (Day 15~28) | Stage 3 (Day 29~35) | TLI/plt | Shoot FW/plt | PY
16 | N1_E1.2_F230_D20 | N1_E1.2_F270_D16 | N1_E0.6_F270_D17 | 12.39 | 136.5 | 11.01
17 |  |  | N2_E1.2_F270_D17 |  | 125.2 | 
18 |  | N2_E1.2_F270_D16 |  |  | 112.4 | 
19 |  |  | N2_E0.6_F270_D17 |  | 104.6 | 
20 | N1_E1.2_F230_D20 | N1_E1.2_F270_D16 | N1_E0.6_LRB_270_D17 | 12.39 | 159.5 | 12.87
21 |  |  | N1_E0.2_LRB_270_D17 |  | 104.2 | 
Treatment no. | Shoot FW/plt, g/plt | TLI/plt, mol/plt | PY, g/mol
The best: no. 20 | 159.5 | 12.39 | 12.87
The worst: no. 4 | 79.89 | 12.04 | 6.63
(12.87-6.63)/6.63 x 100 = 94.1 %
The best vs. the worst:
153
Ｃｏｍｐａｒｉｓｏｎ ｏｎ ｈｉｇｈｅｓｔ ａｎｄ ｌｏｗｅｓｔ ＰＹ

## Slide 154: 7 days prior to harvest, change from FL to LED
DAS =35 days
FL vs. RB LED (7 days prior to harvest)
FW 16.9 % difference (RB LED is better due to spectral difference)
treatments | FW g/plt | TLI mol/plt | ＰY g/mol
20. FL+FL+LED | 159.5 | 12.39 | 12.87
16. FL+FL+FL | 136.5 | 12.39 | 11.01
ＰY= FW/TLI (in g/mol)
FL (CT=3000 K) vs. RB LED (R:B=9:1)

## Slide 155: 7 days prior to harvest, change from FL to LED
Nitrate 8 % difference (RB LED is better due to more RED)
treatment | g/plt | Nitrate ppm
20. FL+FL+LED | 159 (better) | 2291 (better)
16. FL+FL+FL | 136 | 2475
FL (CT=3000 K) vs. RB LED (R:B=9:1)

## Slide 156
Q & A
Line and Wechat ID: weifang0257
    Proper prior planning prevents poor performance