## Slide 1: Environmental control in PFAL Air Temperature, Humidity and Velocity
Wei FANG
Dept. of Biomechatronics Engineering (BME) and Global ATGS
Center of Excellence for Controlled Environment Agriculture (CCEA)
National Taiwan University (NTU)
[ATGS 7140] Plant Factory – Theory and Practice

## Slide 2
Topic 5 involved
Topic 4 involved
Topic 6 involved
air
leaf

## Slide 3: Five governing factors in PFAL (PF with Artificial Lighting no sunlight)
Air
Light
Water
Nutrient
Gas
Wind, Temperature, Humidity
quality
Intensity: PPFD
duration
receipt
concentration: EC
Availability: pH
CO2
concentration
When
Frequency
Dissolved Oxygen
Temperature

## Slide 4: Must have monitoring items
Air Light Gas
Water Nutrient
Light Intensity, quality, duration
T、 RH、Wind
CO2
pH、EC
Tw、DO

## Slide 5: Factors affecting plant growth and development
Temperature
Light
Humidity
Nutrient+H2O
Degree of influence: +++ large, ++ medium, + small
Suitable range in between 15 ~ 30 oC
photosynthesis
respiration
Absorb. of nutrient+H2O
Transpiration
Development (leaf,flower formation)
booming
fruiting
Distribution of sugar
Formation of organ
Extension of cell/organ
Mature of fruit
++
Modified by Fang, 2018

## Slide 6: Outline
Fundamentals
Integrated Approach
Actuators of air control
T, RH, air velocity measurement
A
M
F
I

## Slide 7: Temperature control
to Manipulate Crop Growth and Development.
  Growth is an irreversible increase in mass (dry weight).
  Development is a sequential movement through life stages.
Controlling temperatures involves moving heat into or out of a PFAL. Really though, we are talking about moving heat into or out of a plant to manipulate how it grows and develops.

## Slide 8: Temperature as a tool to manipulate growth and development
Which plant (both are the same age) has the most growth, the most development?
We use temperature to manipulate both growth and development.

## Slide 9: Moving or transferring heat
Conduction
Convection
Thermal Radiation
Evaporation / Transpiration
Heat transfer associated with phase change (liquid to gas)
Latent heat of vaporization
  Water = 540 cal/mL = 540x4.2 J/mL
  High compared to other liquids
Plant cools itself by evaporating water from stomates, termed transpiration
Evaporative cooling pads help cool some buildings
Heat energy released as Electromagnetic Radiation (EMR)
Everything above absolute zero emits electromagnetic radiation
Wein’s law -- As temperature , energy emitted as shorter 
Plant loses most of heat this way
Some greenhouses use radiant heating systems
Air or fluid moves to new location to transfer heat
Chimney effect (Passive ventilation)
  Hot air rises, cold air sinks
Convection oven
Forced air heating and air conditioning
Direct transfer of heat
Kinetic energy transferred due to collisions
Billiard balls, Boiling water on electric stove

## Slide 10: Energy Budget of PFAL = Gains minus Losses
Heat Gains
Solar radiation and ‘trapped’ heat = 0
Heating system = 0
Other machines
  Lamps
  AC systems
  Fan motors
  Pumps
Heat Losses
Conduction
  Direct transfer of heat through thermally insulated walls/roof/floor, assuming = 0
Ventilation/Infiltration
  Loss of heat and openings
  Depends on tightness of the PFAL.
  ACH for PFAL, forced ventilated greenhouse
  ACM for Naturally ventilated greenhouse

## Slide 11: Energy Budget of a Plant in PFAL
Gains
  Radiation (short wavelength) from light source in PFAL
  Thermal radiation (Long wavelength)
  Convection from warm air
Losses
  Thermal radiation (Long wavelength)
  Transpiration
  Convection to cool air

## Slide 12: Energy balance of a leaf
Tleaf > Tair
Tleaf < Tair
Transpiration acquire energy from radiation - convection
Transpiration acquire energy from radiation + convection
More water transpired due to more energy acquired for transpiration
Air movement > 0, RH < 100%
Geelen, Voogt and van Weel, 2020 Plant empowerment
Geelen, Voogt and van Weel, 2020 Plant empowerment

## Slide 13: Determining Greenhouse Heat Requirements
Calculate heat loss from greenhouse
Q = [(A1* x U1) + (A2* x U2)] x (TInside-TOutside) x W x C
  A = Surface Area of exposed walls calculated by grower
  U = Conductance factor - provided by manufacturer
  Ti – T0 = Temperature Differential - calculated from climate data
  W = Wind Factor - calculated from climate data
  C = Construction Factor - provided by manufacturer
Q is how much heat need to be supplied by a heating system.
* The subscript indicates different wall/glazing materials, e.g. wood, glass, concrete, plastics, etc.)
Determining PFAL Heat Requirements
Calculate heat loss from PFAL
Q = 0

## Slide 14: Cooling
Greenhouse
Reduce air temperature through natural or forced ventilation or AC
Replenish CO2
  Outside ~380 ppm, inside can be much lower
Reduce relative humidity
   Condensation on leaves
   Disease
PFAL
Reduce air temperature through AC
Replenish CO2 through CO2 enrichment system
  inside should at least 800 ppm
Reduce relative humidity
   Condensation on leaves
   Disease

## Slide 15: Using temperature to control plant growth

## Slide 16: Temperatures indoor
Air temperature
  Most commonly and easily measured
  Night temperature is easier to control than day temperature
Leaf temperature
  Difficult to measure
  Most likely different (>, =, < ) from air temp
Media temperature
  Roots
  Nutrient solution
  Propagation

## Slide 17: How Temperature Affects Plants
Flower induction in some species
  e.g. Easter lily、Phalaenopsis
Interacts with photoperiod to control floral induction
  Heat delay
Bud dormancy or vernalization
  e.g. hydrangea & azalea
Controls rate of stem elongation
  *Most important

## Slide 18: Adverse Effects of Temperature
Chilling injury often occurs at less than 50°F/10°C
  African violets 紫羅蘭
  Poinsettias 聖誕紅
  Hibiscus 木槿
  Gloxinia 大岩桐
  Tomatoes 蕃茄
  Foliage plants 觀葉植物
  Phalaenopsis 蝴蝶蘭
Chilling injury - membrane dysfunction
  Lipids in tropical and subtropical plant membranes solidify

## Slide 19: Growth vs. Development
Growth
  increase in size (volume or weight) of plant or organ that is irreversible and permanent
Development
  Aging process of the plant – phases that plant goes through as gets older
    Germination
    Vegetative growth
    Flowering
    Fruit set
    Seed release

## Slide 20: Growth Rates of Plants
Growth rate = The speed at which an organ goes through a certain developmental stage
  Stem growth
  Flower production
  Leaf unfolding
All growth processes have different temperature response curves
  Even within species
  Cultivar specific

## Slide 21: Optimal Temperature
Every species has both optimal and tolerable temperature range for growth
Optimal range: produce high quality plants most rapidly
  Mums = 16~17oC (night)
Tolerable range: still grow but more time and lower quality
  Mums = 4-15°C & 18-27°C (night)

## Slide 22: Cumulative Growth
Instantaneous plant temperature controls growth at any moment
Cumulative growth in 24 h = average of individual growth rates during that period
Manipulating average daily temperature in the PFAL (within tolerable range) will change the rate of plant development
  Fast growth  high quality growth

## Slide 23: Average Daily Temperature
Growers have target temps for day and night
Can calculate an average daily temp.
Weighted average
  Day 16 h @ 25°C
  Night 8 h @ 20°C
  Weighted Avg. temp = [(16x25)+(8x20)]/24 = 23.33°C

## Slide 24: Relative growth rate = f(Tdb) Temperature affects growth rate
Maximum is usually not optimum.
Optimum is the temp. that has the plant at the stage you want it to be at!!!!!!
Base temperature : intersection of the straight line (linear range) and the X-axis (X-intercept)
Maximum temperature: peak of growth rate curve
portion of curve that is a straight line
Base temperature

## Slide 25: Relative Growth Rate

## Slide 27: More of the temperature related topics can be found in the sup. of this pptx.
Including concept of Degree-Days
DIF and DROP.
These concepts are used mostly in greenhouse for flowers and ornamental plants, not in PFAL.

## Slide 28: From Psychrometrics, we learned
“Temperature affects humidity”
This is only partially true
Change of Dry bulb temperature affects relative humidity (RH)
But not affects absolute humidity (AH)

## Slide 29: Plant growth and development involved many highly complicated and intercorrelated processes
Tair
Tleaf
Resistant of root, root zone
Water potential difference between root and growth media
root
stem
leaf
plant
etc.
Stomata resistant layer of air and leaf
VPD/AHD between air and leaf affected by T and RH / AH
light
H2O CO2 concentration
Energylight (480 kJ)
Material exchange: H2O, inorganic macro/micro nutrients (N, P, K, …) concentration
Flower
Fruit
materials
2ndary metabolites

## Slide 30: Iso-growth rate=f(Ta, Tw) and other 3 are fixed values
Light Intensity: 20,000 lux
Relative Humidity: 70%
CO2 concentration: 400 ppm
Ta
Tw
Air T: Ta 20 oC
Solution T: Tw 20 oC
Relative growth rate:  = 0.19
Temperature of air (Ta) and nutrient solution (Tw) affects
growth rate
At least 6 factors involved to derive Relative Growth Rate, air movement is the one that is missing

## Slide 31: Influence of air movement

## Slide 32: Pn=f(Air velocity) when Light, RH are fixed How about Ta, Tw, CO2 ? Air Velocity affects photosynthetic rate
Air velocity
Photosynthetic rate

## Slide 35: DM increment = f(Air velocity, RH) when Light and Tdb are fixed, how about CO2 ?
PAR
Cucumber
Tdb
DM increment (g/m2/h)
Air velocity (cm/s)
Air Velocity and RH affects growth rate expressed as hourly DM increment per unit leaf area

## Slide 36
Freshness
Leaf area
Dry mass

## Slide 37
Dry-Base
moisture content
= moisture weight / dry weight
Intersection
  Ta: 20 oC
  Tw: 20 oC
  L: 12 hr
  N: 400 ppm
Air temperature (Ta),
solution temperature (Tw),
day length (L) and
CO2 concentration (N)
affects
moisture content (Wc) and
growth rate, expressed in daily relative DM increment (∆M) and relative FM increment (∆ W)
of the plant
There is no air velocity involved in this study.

## Slide 38: Observation (1/2)
Air T (Ta >24) does not affect moisture content (Wc=25)
Ta @20 has
  best Wc@23
  max daily dry weight increment (∆M)
Ta 22~24 has max daily fresh weight increment (∆W)
Ta 30 drop to 20, ∆M increase
Ta 28 drop to 20, ∆M increase from 0.5 to 2
Solution T (Tw@14~26) greatly affects Wc 15~25
Higher Tw, higher Wc, higher ∆W (0.4 to 1.5)
Tw@20 has greatest ∆M

## Slide 39: Observation (2/2)
CO2 (400~1200 ppm)
  greatly affects Wc (23~15)， higher CO2 (1200), lower Wc (15)
  Greatly affects ∆M, almost in direct proportion
  greatly affects ∆W, but gradually decrease the degree of increment when CO2 increase
Day length (6~24 hrs)
  does not affects Wc
  greatly affects ∆M, almost in direct proportion
  greatly affects ∆W, but gradually decrease the degree of increment when CO2 increase

## Slide 40: Optimum Growth can be reached through various settings in different stages in PFAL. To harvest 200 g FM/plant, required 105 days in open field (Spring / Autumn) and 35 days in PFAL
Optimum Growth Condition
Stages in PFAL
Days after Sowing
Spring/Autumn Open field production
Lettuce 10 ~ 200 g Growth rate greatly enhanced in PFAL
Fresh Mass, g/plant

## Slide 41
Effects of CO2 enrichment is substantially increased when under high PPFD and high air T
300 μmol/s.m2
600
PPFD=900
PPFD=1200
CO2 1000 ppm
CO2 400 ppm

## Slide 43: New trend using Leaf T instead of air T
Geelen, Voogt and van Weel, 2020 Plant empowerment

## Slide 44: Outline
Fundamentals
Integrated Approach
Actuators of air control
T, RH, air velocity measurement
A
M
T
F
I

## Slide 45: Installation/operation guidelines for Temperature measurement
Sensors
  mounted close to plant canopy
  should be shaded
  should have proper ventilation
    Air passing through sensing element
    Air suction at negative pressure
    Air pass through sensing element of Tdb first, then sensing element of Twb

## Slide 46: Dry and wet Bulb Temperature sensors in weather station and greenhouse

## Slide 47
18 ~ 21 oC

## Slide 48: Tdb and RH Sensors

## Slide 49: T&RH sensors installed in PFAL

## Slide 50: T&RH Data logger
(Temperature, Dry Bulb)

## Slide 51: Wind velocity sensors / Anemometer
This type is not suitable for PFAL
A better choice:
Hot-wire anemometer
https://www.eyc-tech.com/show/eyc-hot-wire-type-air-velocity-series-product-principle-application.htm

## Slide 52: Cheapest wind velocity sensor
There are 9 wind velocity sensors can be found in this photo

## Slide 53: Sideward vs. downward air

## Slide 57: Cargo container PFAL for seedling production

## Slide 58: Installation of circular fans
Sideward wind
每層可放四個72/128/288孔穴盤
4 x 72/128/288 plug trays x 4 layers/bench

## Slide 59: Sideward wind: Horizontal fans vs. Regular fans

## Slide 60: Blower + pipe vs. sideward wind

## Slide 61: Without wind within microclimate, lettuce is easy to get tip burn, especially under vigorous growth condition
Tdb 25℃
Outside leaf (old leaf)
Inner leaf (new leaf)
VPD (kPa)
45Ca
Goto and Takakura, 1992a, b
High RH
Low RH
Tip burn is easily to occur on inner leaf due to lack of Ca

## Slide 62
Air velocity（mL/min/plant）
Outside leaf
Inner leaf
Tdb 25℃
RH 76 %
45Ca
Goto and Takakura, 1992a, b
VPD = 0.76 kPa
Tip burn problem can be easily released by providing air velocity.
More reading: https://urbanagnews.com/blog/prevent-tipburn-on-greenhouse-lettuce/

## Slide 63: Outline
Fundamentals
Integrated Approach
Actuators of air control
T, RH and air velocity measurement
A
M
F
I
Air conditioning/dehumidification
Humidification：Humidifier
Air velocity: blower and/or horizontal fan

## Slide 64: Cooling and humidity control Inverter Air Conditioning is preferred
When AC is ON, it also works as a dehumidifier
However, when T is in proper range but still humid, a dehumidifier is still needed.
Inverter AC system
Traditional AC system

## Slide 65: COP of an Inverter AC system
COP
The electricity cost on AC system depends on the COP value. The sole cooling load in a well thermally insulated PFAL will be the heat from light source.
Assuming the COP is 5, the electricity cost of the AC system will be 20% (1/5) of the operating cost of the light.

## Slide 66: How to operate the AC system in PFAL?
  Assuming D/N temperature settings at 23/18 oC
One AC system
  set at night setting: 18 oC
  Day period: indoor T < 22 oC turn off, > 24 oC turn on
  Night period: Let AC controller work automatically
  D/N temperature difference can be reached through on/off of the light source. TFL: 5 degree difference, LED: 2~3 degree difference
Two AC systems
  Both set at 18 oC
  It is better to choose AC with Reset settings after power break off
  Day period: indoor T < 22 oC turn off, > 24 oC turn on
  Night period: Let AC controller work automatically
23 + 1

## Slide 67: Overcome AC system with no reset settings use infra-red to mimic press down of ON button

## Slide 68: PFAL with no humidifier
With any hydroponic system using water culture, RH can be increase by just evaporation from the nutrient solution surface. For such system, humidifier might not be necessary.
As shown in the left diagram, RH might be too low for plant growth. It is better to turn on humidifier.

## Slide 69: PFAL with humidifier
72 ~ 78 %
1. Spinning atomizer
2. Ultrasonic humidifier
3. Pad and fan
As shown above, 3 types of humidifiers were developed.
condensed fog was scrape off with multi-layer nets

## Slide 70: Spinning Atomizer
Circulating fan should be used together with humidifier

## Slide 71: Ultrasonic humidifier
Circulating fan should be used together with humidifier

## Slide 72: Pad and Fan for humidification

## Slide 73: Controller using PLC

## Slide 74: Menu page of the touch screen

## Slide 75: Light control page of the touch screen

## Slide 76: Pump control page of the touch screen

## Slide 77: Temperature/Humidity control page of the touch screen

## Slide 78: Temperature control
Chilled water T
Air Temperature

## Slide 79: Humidity control
Air Temperature
Air Humidity

## Slide 80: CO2 control page of the touch screen

## Slide 81: CO2 control

## Slide 82: Cloud based design
TCP/IP
TCP/IP
TCP/IP
Dropbox
(Excel)
遠端副PC
遠端主PC
PLC

## Slide 83: Remote Control Software

## Slide 84: Outline
Fundamentals
Integrated Approach
Actuators of air control
T, RH and air velocity measurement
A
M
F
I

## Slide 85: Improvement of NTU PFAL performance
Reduction of Air change per hour (ACH)
Replace TFLs to LEDs
Wind velocity to reduce vertical T difference and improve uniformity
Humidity control
CO2 control
EC、pH control
Remote control

## Slide 86: 1. Temperature control
Goals:
To reduce vertical temperature difference
To increase temperature uniformity
Before
  Vertical temperature difference reaches 5°C
  Poor uniformity on temperature distribution per layer

## Slide 87: Improvement on temperature
After
  Temperature of each layers reduced, especially in the upper layer
  Uniformity on temperature distribution per layer increase

## Slide 88: Uniformity on Temperature
Before
After

## Slide 89
2. Humidity control
RH
Sensor
PLC
AD module
PLC (PID)
PLC (PWM )
Humidifier

## Slide 90: Future work: From RH to AHD control
VPdif of the air and leaf
  VP of Tleaf – VP @Tdb,RH
AHdif of the air and leaf
  AH of Tleaf –AH @Tdb,RH
VPD and Stomata opening
which one is the cause and which one is the outcome?
Geelen, Voogt and van Weel, 2020 Plant empowerment

## Slide 91
3. CO2 enrichment
CO2 Sensor
PLC
AD module
PLC (PID)
PLC (PWM)
Valve

## Slide 92
4. Nutrient control
pH、EC
Sensors & transmitter
PLC
AD module
PLC (PID controller
PLC (PWM)
Peristaltic pump

## Slide 93
5. Remote site: User Interface

## Slide 94: 6. Keep proper Air tightness of PFAL
Air change/minute (ACM) & ACH (AC/hour) as the index
ACM around 0.8~1 for forced air ventilated greenhouse
ACH range from 0~20 for naturally ventilated greenhouse
ACH no more than 0.01 in PFAL
High ACH means
  loss of CO2 enriched cooled humid air
  low resource utilization efficiency on CO2 , energy and water.

## Slide 95
There are no plants and no workers in the PFAL/NVGH/TC. Vessel
Enrich CO2 indoor to reach high concentration
NVGH: 3~4000 ppm
PFAL: 8000 ppm
Tissue Culture Vessel (T.C. vessel): 10000 ppm
Allow the CO2 concentration to drop naturally.
Outdoor CO2 concentration is C0
Measuring the indoor CO2 concentration in real time if possible
NVGH, PFAL, real time measurement is preferred
T.C. vessel: 30 min to 1 hour interval
Track the Time and the CO2 concentration for at least 2 points (T1, C1; T2,C2)
with at least one hour interval
Steps to measure ACH

## Slide 96
Measuring ACH
N=ln((C1-C0)/(C2-C0)) / T
where,
ln: natural log
T=abs(T2 - T1) (in h)
Time is the X axis,
Y is natural log of CO2 concentration difference at Ti minus Co
N is the slope
T1=2, T2=3
C0=360, C1=10000, C2=4000 (ppm)
→N=ln(9640/3640)/(3-2) = 0.97/h
T2
T1

## Slide 97: PFAL with high air tightness and thermal insulated walls to ensure High Resource Utilization Efficiency (RUE)
High degree of tightness ensures high CO2 concentration indoor. With min loss to outdoor, high RUE of CO2 can be reached.
Water vapor transpired from the plant can be condensed by AC system and reused to ensure high RUE of water.
Thermally insulated walls allowed min heat from outdoor, no heating required and cooling load is the heat from light source. An AC system with a COP of 4, the elec.cost on AC will be ¼ of the lighting cost.
In light period, AC system will maintain RH at around 60-70%, which is close to optimum。

## Slide 98
ACH = 0.01 h-1
RUE of CO2 = 0.87
ACH = 0.06 h-1
RUE of CO2 = 0.21
RUE of CO2
Supplied
Leak
Fixed
0.06
175
46
46/221 = 0.21
RUE of CO2
Supplied
Leak
Fixed
High degree of tightness ensures high CO2 concentration indoor. With min loss to outdoor, high RUE of CO2 can be reached

## Slide 99
ACH = 0.01 h-1
with Reuse
RUE of Water = 0.985
without Reuse
RUE of water = 0.273
Water vapor transpired from the plant can be condensed by AC system and reused to ensure high RUE of water.
1186
RUE of water with REUSE
Irrigated
Leak
P: increase of water in plant 42
S: increase of water in substrate 414
Leak to outdoor: 39
Amount of water condensed by AC: 1186
ACH = 0.01 h-1
RUE of water without REUSE
Irrigated
Leak
P: increase of water in plant 42
S: increase of water in substrate 414
Leak to outdoor: 39
Amount of water condensed by AC: 1186
42 +414
0.273
ACH = 0.01 h-1
P + S

## Slide 100: 7. PFAL cleanliness: Clean room standard
Clean rooms are classified according to the cleanliness level of the air inside the controlled environment.
The clean room class is the level of cleanliness the room complies with, according to the quantity and size of particles per cubic meters of air. The primary authority in the US and Canada is the ISO classification system ISO 14644-1.

## Slide 101: PFAL dust free class
Class A
Dust Free Room
PFAL

## Slide 102: Particle counter

## Slide 103: Integrated Approach
Wind velocity at proper range 0.5~1.2 m/s
Air temperature keep at proper range
Clean room standard to maintain minimum bacteria counts
CO2 keep at 1000~2000 ppm
DLI ≈ 14 for leafy veg. & ≈ 17 mol/m2 semi-head veg.
Tightness of PFAL, ACH keep at no more than 0.01
RH keep at 70~85% (VPD at proper range)
L
C
H
A
W
T
B
Notes: maintain

## Slide 104: Integrated Control
A: Temperature control
B: Air velocity control
C: CO2 control
D: VPD/AHD control
E: Nutrient control
Light Intensity
Pn
Buckets effect
Cannikin Law

## Slide 105: XX company vs. NTU PFAL
Items | XX | NTU PFAL
D/N Temp. difference | No | Yes
DLI DL PPFD | low 10~12 h/day < 150 mol/m2/s | proper 16 h/day > 200 mol/m2/s
Humidity control | No | Yes
Wind velocity | No | 0.5 ~ 1 m/s
CO2 enrichment | No | 1200 ppm
EC level | 1.8 mS/cm (manual) | 1.2 mS/cm (Auto)
Harvested at | DAS=44 | DAS=35
FM/plant | 60 ~ 75 g/plant | 120 ~ 140 g/plant

## Slide 106: Conclusion
Temperature control plays major role in GH
Light control is of great importance in PFAL
Three under-emphasize factors
  Absolute humidity (AH) is a better index than relative humidity (RH) to estimate water balance
  Adequate wind velocity (0.3~1.0 m/s) to ensure better uniformity and gas exchange around micro-environment of the plants
  Tightness of PFAL should be kept, ACH no more than 0.01

## Slide 107: The END

## Slide 108: Supplements
Degree-Days
DIF
DROP
Mostly frequent used in greenhouse, not in PFAL.

## Slide 109: Degree-day Concept
Slope: Dy/Dx Change in growth rate / change in temp
    e.g.# leaves/day/°F → leaf unfolding
    e.g. inches/day/°F → stem elongation
Daily increase in leaf production or stem elongation as you raise the average temp 1°F

## Slide 110: Degree-day Concept
The amount of heat (or degree-days) above the base temp that must accumulate for a developmental event to occur
1 degree-day will accumulate when the day’s average temp is 1°F above base temp
  Average temp = 55°F
  Base temp = 50°F
  5 degree-days will accumulate that day

## Slide 111: Degree-day Concept
Degree-day constant associated with every development stage
  e.g. 80 degree-days needed to reach a certain stage
All of the following would accumulate 80 degree-days
  80 days @ 1° above base temp
  40 days @ 2° above base temp
  8 days @ 10° above base temp
Allows crop growers to schedule and time crop development

## Slide 112: Application of Degree-days (hypothetical numbers)
Easter Lily production during leaf development
  Slope = 0.02 leaves/degree-day
  Degree-day constant = 1/0.02 ≈50
    50 degree-days/leaf
  What temp to produce 3 leaves in 10 days?
  Avg daily temp = total degree-days + Tbase*
  desired time
  * Tbase = base temperature

## Slide 113: Example cont’d
What avg. daily temp to produce 3 Easter lily leaves in 10 days?
  Base temp = 55°F
Avg temp = 3 x 50 + 55
10
Maintain 70F avg. temp and you should have 3 new leaves in 10 days!
≈ 70F

## Slide 114
Most E. Lily growers use a ‘bud meter’ once flower buds are visible
By measuring the length of the bud, the grower knows how warm to keep the greenhouse to get the bud to the selling stage by Easter. The bud meter is based on degree days.

## Slide 115: Graphical Tracking
Let you know where your crop is compared to where it should be in height
IMPORTANT because of shipping container size and aesthetic appeal of crop

## Slide 116
Above this line, plants too tall, need growth regulation
Below this line, plants too short, need to elongate plant
Pot height
Graphical tracking used to determine temperature requirements and other growth regulating practices.
Acceptable finished height.
Measure representative plants once or twice a week and adjust growing techniques accordingly.
Before and just after visible bud is usually when plants are most responsive to growth regulation.
Above this line, plants too tall, need growth regulation
Below this line, plants too short, need to elongate plant
Pot height

## Slide 117: Original Applications of Degree-days
Field-grown crops
  Count degree-days by measuring temp
  Predict days to harvest
    Apples: bloom → harvest = 2800 degree-days
  Predict insect hatching/molting
Degree-days = (Tmax – Tmin)/2 – Tbase
Prediction only - growers of field-grown crops have no control over temperature

## Slide 118: History of DIF
Originally discovered in 1944
“Rediscovered” and developed as a growth regulation technique in late 1980’s by Dr. Royal Heins at MSU
The DIFference between day and night temperature in a greenhouse will affect internode elongation and consequently, stem length.
DIF for Temperature and Growth (stem height) Regulation

## Slide 119: DIF = Day temp – Night temp
+ DIF when Day temp > Night temp
0 DIF when Day temp = Night temp
- DIF when Day temp < Night temp
DIF effects on internode elongation Within normal growing temperatures, the more positive the DIF, the longer the internodes.

## Slide 120
Greenhouse | A | B | C
Day temp | 60°F | 55°F | 50°F
Night temp | 50°F | 55°F | 60°F
Avg. Daily temp | 55°F | 55°F | 55°F
DIF | +10 | 0 | -10
Internode length (plant height) | Tall | Medium | Short

## Slide 121: DIF Responding Species
Easter lilies 百合
Poinsettias 聖誕紅
Snapdragon 金魚藻
Rose 玫瑰
Petunia 牽牛花
Carnation 康乃馨
Impatiens 鳳仙花
Tomato 蕃茄
Pepper 小黃瓜
DO NOT RESPOND
Hyancith 風信子
Tulip 鬱金香
Narcissus 水仙
Squash 南瓜

## Slide 122: Degree-days vs. DIF
Avg. daily temp (or degree-day accumulation) control rate of plant development
DIF responsible only for plant height regulation (internode elongation)
  More positive DIF → the taller the plant
  More negative DIF → the shorter the plant

## Slide 123
 | A | B | C
Day temp | 60°F | 55°F | 50°F
Night temp | 50°F | 55°F | 60°F
Avg. Daily temp | 55°F | 55°F | 55°F
DIF | +10 | 0 | -10
Internode length (plant height) | Tall | Medium | Short
Which greenhouse would have the tallest plants? The shortest? The furthest along in development?

## Slide 124: Side Effects of Extreme –DIF
Chlorosis (esp. DIF < -10F)
  Bedding plants (e.g. salvia)
Leaf orientation
  Problem on Easter Lily
  (photos courtesy of Dr. Harold Wilkins)

## Slide 125: Other effects of DIF
DIF response is quick and reversible
  Adverse effects of –DIF can be fixed with a few days of 0 or + DIF
  Effects show up quickly
DIF and photoperiod
  As daylength , greater response to –DIF

## Slide 126: Limitations of DIF
Flower initiation
  Poinsettia inhibited to flower at night temps above 72°F (22.2oC)
Seasons
  -DIF is not always achievable
  Summer in warm climates
  Sunny, clear days heat up greenhouse

## Slide 127: DROP
Lowering temp first few hrs of day
  More effective than lowering temp at the end of day
  Majority of stem elongation occurs in these first morning hrs
  Combining a morning DROP with slight – or 0 DIF is better than more –DIF
  Drawing back thermal blanket or ventilating before sunrise, good way to achieve DROP

## Slide 128
Midnight
8:00 pm
Noon
Temp.
Typical DROP daily temperature pattern