## Slide 1: Development of modified photostationary state model to relate phytochrome conversion and flowering of spinach 光敏素調節開花機制的數學模式 —以菠菜開花為例
Wei FANG 方 炜 Zong Han YANG 杨宗翰
Dept. of Biomechatronics Engineering 生物机电工程系
National Taiwan University 台湾大学

## Slide 2
Energy sources
(Photosynthesis)
Signal sources
(Photoperiod)
(Photomorphogenesis)
Light: Sun light or artificial light

## Slide 3
PAR (PPFD)
BAR (BPFD)
Biologically Active Radiation in W/m2
B.A.Range: 300 ~ 800 nm
Biological Photon Flux Density, μmol/m2.s
Photosynthetic Photon Flux Density, μmol/m2.s
Photosynthetically Active Radiation in W/m2
P.A.Range: 400 ~ 700 nm

## Slide 4
Phytochrome conversion
Active form
Inactive form
Dark

## Slide 5
Photoreceptors

## Slide 6
Yield Photon Flux (YPF)
Nλ：Spectral photon distribution (SPD)
：Relative quantum efficiency
Relative Quantum Efficiency
Sager et al,1988

## Slide 7: One equation with various names
Phytochrome PhotoEquilibrium, PPE
Phytochrome Photostationary State, PPS
Phytochrome photoStationary State, PSS
PhotoStationary State, PSS
PSS, PPE, PPS ＝

## Slide 8
Phytochrome photoStationary State
PSS ＝
Far red promotes Pfr  Pr
Less no. of Pfr lead to smaller PSS
Red promotes Pr  Pfr
Many Pfr lead to bigger PSS

## Slide 9
Butler et al., 1964
Pratt and Briggs 1966
Sager et al., 1988
Kelly and Lagarias, 1985

## Slide 10
(Morgan and Smith., 1976)
PSS vs. Photomorphogenesis
藜 Fat hen
PSS
Higher PSS, lower extension rate

## Slide 11
(Child and Smith., 1987)
PSS vs. Photomorphogenesis
(Morrow and Tibbitts., 1988)
Tomato
Phytochrome PhotoEquilibrium, PPE
Higher PSS, lower extension rate
Higher PSS, more tumors
Mustard (Sinapis alba)

## Slide 12
Kalaitzoglou et al., 2019
PSS vs. stem elongation
Tomato
Higher PSS, lower plant

## Slide 13
PSS or PPS
Sun to shade: 0~1
Sun to shade: 1~0

## Slide 14
CW
HPS

## Slide 15
Stem elongation

## Slide 17: Predicting Stem Elongation and Leaf Expansion: Percent far-red is a better predictor than PPE
I disagree
% far-red and PPE/PSS/PPS are similar predictors

## Slide 18
Photochemical crosssection
σr
σfr
PhotoStationary State, PSS
PSS ＝
Sager et al,1988
K1
K2
Sager et al,1988

## Slide 19
Objective
PSS
Light Period
T@L/D: 20 oC/
oC/
CW
CW
Dark Period
18 oC
23 oC
FR
LP: 12, 13, 14 h
Investigate on PSS vs. flowering ratio
Spinach: Long-day plant
Light Period@11 h, no flowering
To inhibit flowering, FR is needed.
To promote flowering, R and LD are needed.
Targets: LD, no flowering, increased FW
+FR
FR

## Slide 20
Treatments
Totally 21 treatments with two dark period temperature (DT) and FR in dark or light period.
Totally 11 treatments with DT = 18℃ and FR in dark period.
Temperature : 20/18℃
Temperature : 25/23℃
FR (50 μmol m-2 s-1 x 2)
FR (50 μmol m-2 s-1 x 2
with diffuse film)
FR (50 μmol m-2 s-1 x 4)
FR (25 μmol m-2 s-1 x 4)
12 14
12 14
14 16

## Slide 21
Photosynthetic rate
Growth rate
Photomorphogenesis
fresh/dry weight
extension/elongation rate
tumor area
Flowering ratio

## Slide 22
Daily Integral of PhotoStationary State model (PSS’ )
NCWλ：Light intensity of CW LED at λ nm, in mol·m2·s-1
σrλ：The photochemical cross section of Pr at λ nm, in m2 mol-1
K1(CW)：Conversion rate of Pr to Pfr under white light, in µs-1
σfrλ：The photochemical cross section of Pfr at λ nm, in m2 mol-1
K2(CW)： Conversion rate of Pfr to Pr under white light, in µs-1
NFRλ： Light intensity of FR LED at λ nm, in mol·m2·s-1
K1(FR)： Conversion rate of Pr to Pfr under far-red light, in µs-1
K2(FR)： Conversion rate of Pfr to Pr under far-red light, in µs-1
LCW：Duration of CW LED, in hour/day
LFR： Duration of Far-red LED, in hour/day
K1I：Integral of active form phytochrome throughout light period
K2I：Integral of inactive form phytochrome throughout light period

## Slide 23
PSS′
Treatment | PSS′ | Flowering ratio
6CW (12)_4FR (2) 25/23℃ | 0.7629 | 6.67%
6CW (12)_4FR (2) 20/18℃ | 0.7571 | 6.67%
6CW (12)_4FR (1) 25/23℃ | 0.7889 | 20.00%
6CW (12)_4FR_half (2) 25/23℃ | 0.7913 | 26.67%
6CW (12)_2FR (2) 20/18℃ | 0.7741 | 27.27%
6CW (12)_2FR_diffuse (2) 20/18℃ | 0.782 | 27.27%
6CW (12)_4FR (1) 20/18℃ | 0.7916 | 27.27%
6CW (12)_4FR_half (2) 20/18℃ | 0.7904 | 36.36%
6CW (13)_4FR (4) 25/18℃ | 0.7118 | 46.15%
6CW (12) 20/18℃ (CK) | 0.8344 | 58.33%
6CW (13)_4FR (3) 25/18℃ | 0.7398 | 64.29%
6CW (13)_4FR (2) 25/18℃ | 0.7668 | 66.67%
6CW (14)_4FR (3) 20/18℃ | 0.7465 | 85.00%
6CW (14)_4FR (4) 20/18℃ | 0.7189 | 90.00%
6CW (14)_4FR (2) 20/18℃ | 0.7664 | 95.00%
6CW (14)+4FR (2) 20/18℃ | 0.7662 | 95.00%
6CW (14)+4FR (4) 20/18℃ | 0.7027 | 100.00%
6CW (14)+4FR (3) 20/18℃ | 0.7247 | 100.00%
6CW (14)+4FR_half (4) 20/18℃ | 0.756 | 100.00%
6CW (14)+4FR_half (3) 20/18℃ | 0.7848 | 100.00%
6CW (14)+4FR_half (2) 20/18℃ | 0.8033 | 100.00%
Flowering ratio

## Slide 24
Treatment | PSS | Flowering ratio
6CW (12)_4FR (2) 25/23℃ | 0.7629 | 6.67%
6CW (12)_4FR (2) 20/18℃ | 0.7571 | 6.67%
6CW (12)_4FR (1) 25/23℃ | 0.7889 | 20.00%
6CW (12)_4FR_half (2) 25/23℃ | 0.7913 | 26.67%
6CW (12)_2FR (2) 20/18℃ | 0.7741 | 27.27%
6CW (12)_2FR_diffuse (2) 20/18℃ | 0.782 | 27.27%
6CW (12)_4FR (1) 20/18℃ | 0.7916 | 27.27%
6CW (12)_4FR_half (2) 20/18℃ | 0.7904 | 36.36%
6CW (13)_4FR (4) 25/18℃ | 0.7118 | 46.15%
6CW (12) 20/18℃ (CK) | 0.8344 | 58.33%
6CW (13)_4FR (3) 25/18℃ | 0.7398 | 64.29%
6CW (13)_4FR (2) 25/18℃ | 0.7668 | 66.67%
6CW (14)_4FR (3) 20/18℃ | 0.7465 | 85.00%
6CW (14)_4FR (4) 20/18℃ | 0.7189 | 90.00%
6CW (14)_4FR (2) 20/18℃ | 0.7664 | 95.00%
6CW (14)+4FR (2) 20/18℃ | 0.7662 | 95.00%
6CW (14)+4FR (4) 20/18℃ | 0.7027 | 100.00%
6CW (14)+4FR (3) 20/18℃ | 0.7247 | 100.00%
6CW (14)+4FR_half (4) 20/18℃ | 0.756 | 100.00%
6CW (14)+4FR_half (3) 20/18℃ | 0.7848 | 100.00%
6CW (14)+4FR_half (2) 20/18℃ | 0.8033 | 100.00%
Treatment |  | Flowering ratio
6CW (12)_4FR (2) 25/23℃ | 0.7629 | 6.67%
6CW (12)_4FR (2) 20/18℃ | 0.7571 | 6.67%
6CW (12)_4FR (1) 25/23℃ | 0.7889 | 20.00%
6CW (12)_4FR_half (2) 25/23℃ | 0.7913 | 26.67%
6CW (12)_2FR (2) 20/18℃ | 0.7741 | 27.27%
6CW (12)_2FR_diffuse (2) 20/18℃ | 0.782 | 27.27%
6CW (12)_4FR (1) 20/18℃ | 0.7916 | 27.27%
6CW (12)_4FR_half (2) 20/18℃ | 0.7904 | 36.36%
6CW (13)_4FR (4) 25/18℃ | 0.7118 | 46.15%
6CW (12) 20/18℃ (CK) | 0.8344 | 58.33%
6CW (13)_4FR (3) 25/18℃ | 0.7398 | 64.29%
6CW (13)_4FR (2) 25/18℃ | 0.7668 | 66.67%
6CW (14)_4FR (3) 20/18℃ | 0.7465 | 85.00%
6CW (14)_4FR (4) 20/18℃ | 0.7189 | 90.00%
6CW (14)_4FR (2) 20/18℃ | 0.7664 | 95.00%
6CW (14)+4FR (2) 20/18℃ | 0.7662 | 95.00%
6CW (14)+4FR (4) 20/18℃ | 0.7027 | 100.00%
6CW (14)+4FR (3) 20/18℃ | 0.7247 | 100.00%
6CW (14)+4FR_half (4) 20/18℃ | 0.756 | 100.00%
6CW (14)+4FR_half (3) 20/18℃ | 0.7848 | 100.00%
6CW (14)+4FR_half (2) 20/18℃ | 0.8033 | 100.00%
PSS′
Flowering ratio

## Slide 25
Coefficient of determination (R2)
Daily Integral PhotoStationary State model (PSS′)
Groups | R2 (PSS vs. Flowering ratio)
Totally 21 treatments with various dark temp., duration of light period, intensity of CW and FR, FR concurrent with CW or FR in dark period only. | 0.0943
Totally 11 treatments with FR at dark period and DT @ 18℃ | 0.2014
Groups | 
Totally 21 treatments with various dark temp., duration of light period, intensity of CW and FR, FR concurrent with CW or FR in dark period only. | 0.0943
Totally 11 treatments with FR at dark period and DT @ 18℃ | 0.2014

## Slide 26
In previous models (PSS and PSS’), thermal reversion was missing.

## Slide 27
Phytochromes function as thermosensors
Legris et al., 2017
= 1.79 hours
= 0.86 hours
Jung et al., 2016
Thermal reversion
Half life of Pfr @ dark period
No. of Pfr retained after LN hrs of dark period @ T oC

## Slide 28
Temperature calibrated PhotoStationary State model (T-PSS )
K1(CW)：Conversion rate of Pr to Pfr under white light, in µs-1
K2(CW)： Conversion rate of Pfr to Pr under white light, in µs-1
K1(FR)： Conversion rate of Pr to Pfr under far-red light, in µs-1
K2(FR)： Conversion rate of Pfr to Pr under far-red light, in µs-1
LCW：Duration of CW LED, in hour/day
LFR： Duration of Far-red LED, in hour/day
K1I：Integral of active form phytochrome throughout light period
K2I：Integral of inactive form phytochrome throughout light period
T-PSS
T：Temperature in dark period, in ℃
LN：Duration of dark period (with Far-red LED hours), in hour
t1/2：Temperature-responsive half-life period for Pfr, in hour

## Slide 29
T-PSS
Treatment | T-PSS | Flowering ratio
6CW (12)_4FR (2) 25/23℃ | 0.0029 | 6.67%
6CW (12)_4FR (2) 20/18℃ | 0.0326 | 6.67%
6CW (12)_4FR (1) 25/23℃ | 0.0030 | 20.00%
6CW (12)_4FR_half (2) 25/23℃ | 0.0030 | 26.67%
6CW (12)_2FR (2) 20/18℃ | 0.0333 | 27.27%
6CW (12)_2FR_diffuse (2) 20/18℃ | 0.0336 | 27.27%
6CW (12)_4FR (1) 20/18℃ | 0.0340 | 27.27%
6CW (12)_4FR_half (2) 20/18℃ | 0.0340 | 36.36%
6CW (13)_4FR (4) 25/18℃ | 0.0398 | 46.15%
6CW (12) 20/18℃ (CK) | 0.0359 | 58.33%
6CW (13)_4FR (3) 25/18℃ | 0.0414 | 64.29%
6CW (13)_4FR (2) 25/18℃ | 0.0429 | 66.67%
6CW (14)_4FR (3) 20/18℃ | 0.0542 | 85.00%
6CW (14)_4FR (4) 20/18℃ | 0.0522 | 90.00%
6CW (14)_4FR (2) 20/18℃ | 0.0557 | 95.00%
6CW (14)+4FR (2) 20/18℃ | 0.0557 | 95.00%
6CW (14)+4FR (4) 20/18℃ | 0.0511 | 100.00%
6CW (14)+4FR (3) 20/18℃ | 0.0527 | 100.00%
6CW (14)+4FR_half (4) 20/18℃ | 0.0549 | 100.00%
6CW (14)+4FR_half (3) 20/18℃ | 0.0570 | 100.00%
6CW (14)+4FR_half (2) 20/18℃ | 0.0584 | 100.00%
Flowering ratio

## Slide 30
Treatment | T-PSS | Flowering ratio
6CW (12)_4FR (2) 25/23℃ | 0.0029 | 6.67%
6CW (12)_4FR (2) 20/18℃ | 0.0326 | 6.67%
6CW (12)_4FR (1) 25/23℃ | 0.0030 | 20.00%
6CW (12)_4FR_half (2) 25/23℃ | 0.0030 | 26.67%
6CW (12)_2FR (2) 20/18℃ | 0.0333 | 27.27%
6CW (12)_2FR_diffuse (2) 20/18℃ | 0.0336 | 27.27%
6CW (12)_4FR (1) 20/18℃ | 0.0340 | 27.27%
6CW (12)_4FR_half (2) 20/18℃ | 0.0340 | 36.36%
6CW (13)_4FR (4) 25/18℃ | 0.0398 | 46.15%
6CW (12) 20/18℃ (CK) | 0.0359 | 58.33%
6CW (13)_4FR (3) 25/18℃ | 0.0414 | 64.29%
6CW (13)_4FR (2) 25/18℃ | 0.0429 | 66.67%
6CW (14)_4FR (3) 20/18℃ | 0.0542 | 85.00%
6CW (14)_4FR (4) 20/18℃ | 0.0522 | 90.00%
6CW (14)_4FR (2) 20/18℃ | 0.0557 | 95.00%
6CW (14)+4FR (2) 20/18℃ | 0.0557 | 95.00%
6CW (14)+4FR (4) 20/18℃ | 0.0511 | 100.00%
6CW (14)+4FR (3) 20/18℃ | 0.0527 | 100.00%
6CW (14)+4FR_half (4) 20/18℃ | 0.0549 | 100.00%
6CW (14)+4FR_half (3) 20/18℃ | 0.0570 | 100.00%
6CW (14)+4FR_half (2) 20/18℃ | 0.0584 | 100.00%
T-PSS
Flowering ratio

## Slide 31
Coefficient of determination (R2)
Temperature calibrated PSS (T-PSS)
Groups | R2 (T-PSS vs. Flowering rate)
Totally 21 treatments with various dark temp., duration of light period, intensity of CW and FR, FR concurrent with CW or FR in dark period only. | 0.7397
Totally 11 treatments with FR at dark period and DT @ 18℃ | 0.9222

## Slide 32
Red
T-PSS
Far-red
Textbook
Red and Far-red
UV+PPFD+FR
Is that necessary to use all the data from 300 to 800 nm ?

## Slide 33
Advanced analysis of T-PSS
Three ranges
K1 & K2: 300~800 nm (from UV to FR)
K1 & K2: 600~800 nm (R and FR)
K1: 600~700 nm (R)
K2: 700~800 nm (FR)

## Slide 34
Groups | K1, K2 300~800 nm | K1, K2 600~800 nm | K1: 600~700 K2: 700~800 nm | 
 | R2 (T-PSS vs. Flowering rate) |  |  | 
Totally 21 treatments with various dark temp., duration of light period, intensity of CW and FR, FR concurrent with CW or FR in dark period only. | 0.7397 | 0.732 |  | 0.7267
Totally 11 treatments with FR at dark period and DT @ 18℃ | 0.9222 | 0.9201 |  | 0.917
Advanced analysis of T-PSS

## Slide 35
D-PSS
PPFDR：The average amount of red light during the growing period, in µmol·m2·s-1
LCW：Duration of CW LED, in hour/day
DLIR：Daily light integral of red light (600~700 nm) , in mol·m-2/day
BPFDFR：The average amount of far-red light during the growing period, in µmol·m2·s-1
LFR： Hours of Far-red LED, in hour/day
DLIFR： Daily light integral of far-red light (700~800 nm) , in mol·m-2/day
DPSS：Photostationary state based on DLI
C：Ratio of conversion rate of inactive vs. active phytochrome, C = 3.54
T： Temperature in dark period, in ℃
LN：Duration of dark period (with Far-red LED hours), in hour
t1/2：Temperature-responsive half-life period for Pfr, in hour
含温度校正的简化版光稳态平衡模式 Temperature calibrated DLI based PSS (D-PSS)

## Slide 36: Ratio of conversion rate of inactive vs. active phytochrome, C
C equals ratio of the photochemical cross-section σr and σfr of Pr and Pfr in R and FR waveband, respectively.
Photochemical cross section
σr
σfr
Sager et al.,1988

## Slide 37
Treatment | D-PSS | Flowering ratio
6CW (12)_4FR (2) 25/23℃ | 0.0034 | 6.67%
6CW (12)_4FR (2) 20/18℃ | 0.0390 | 6.67%
6CW (12)_4FR (1) 25/23℃ | 0.0036 | 20.00%
6CW (12)_4FR_half (2) 25/23℃ | 0.0036 | 26.67%
6CW (12)_2FR (2) 20/18℃ | 0.0399 | 27.27%
6CW (12)_2FR_diffuse (2) 20/18℃ | 0.0402 | 27.27%
6CW (12)_4FR (1) 20/18℃ | 0.0407 | 27.27%
6CW (12)_4FR_half (2) 20/18℃ | 0.0406 | 36.36%
6CW (13)_4FR (4) 25/18℃ | 0.0465 | 46.15%
6CW (12) 20/18℃ (CK) | 0.0430 | 58.33%
6CW (13)_4FR (3) 25/18℃ | 0.0491 | 64.29%
6CW (13)_4FR (2) 25/18℃ | 0.0504 | 66.67%
6CW (14)_4FR (3) 20/18℃ | 0.0644 | 85.00%
6CW (14)_4FR (4) 20/18℃ | 0.0624 | 90.00%
6CW (14)_4FR (2) 20/18℃ | 0.0662 | 95.00%
6CW (14)+4FR (2) 20/18℃ | 0.0664 | 95.00%
6CW (14)+4FR (4) 20/18℃ | 0.0611 | 100.00%
6CW (14)+4FR (3) 20/18℃ | 0.0628 | 100.00%
6CW (14)+4FR_half (4) 20/18℃ | 0.0658 | 100.00%
6CW (14)+4FR_half (3) 20/18℃ | 0.0675 | 100.00%
6CW (14)+4FR_half (2) 20/18℃ | 0.0688 | 100.00%
D-PSS
Flowering ratio

## Slide 38
Treatment | D-PSS | Flowering ratio
6CW (12)_4FR (2) 25/23℃ | 0.0034 | 6.67%
6CW (12)_4FR (2) 20/18℃ | 0.0390 | 6.67%
6CW (12)_4FR (1) 25/23℃ | 0.0036 | 20.00%
6CW (12)_4FR_half (2) 25/23℃ | 0.0036 | 26.67%
6CW (12)_2FR (2) 20/18℃ | 0.0399 | 27.27%
6CW (12)_2FR_diffuse (2) 20/18℃ | 0.0402 | 27.27%
6CW (12)_4FR (1) 20/18℃ | 0.0407 | 27.27%
6CW (12)_4FR_half (2) 20/18℃ | 0.0406 | 36.36%
6CW (13)_4FR (4) 25/18℃ | 0.0465 | 46.15%
6CW (12) 20/18℃ (CK) | 0.0430 | 58.33%
6CW (13)_4FR (3) 25/18℃ | 0.0491 | 64.29%
6CW (13)_4FR (2) 25/18℃ | 0.0504 | 66.67%
6CW (14)_4FR (3) 20/18℃ | 0.0644 | 85.00%
6CW (14)_4FR (4) 20/18℃ | 0.0624 | 90.00%
6CW (14)_4FR (2) 20/18℃ | 0.0662 | 95.00%
6CW (14)+4FR (2) 20/18℃ | 0.0664 | 95.00%
6CW (14)+4FR (4) 20/18℃ | 0.0611 | 100.00%
6CW (14)+4FR (3) 20/18℃ | 0.0628 | 100.00%
6CW (14)+4FR_half (4) 20/18℃ | 0.0658 | 100.00%
6CW (14)+4FR减半 (3) 20/18℃ | 0.0675 | 100.00%
D-PSS
Flowering ratio

## Slide 39
Determination coefficient (R2) of three PSS models on flowering ratio
Groups | PSS | T-PSS 300~800 nm | T-PSS 600~700 & 700~800 nm | D-PSS
Totally 21 treatments with various dark temp., duration of light period, intensity of CW and FR, FR concurrent with CW or FR in dark period only. | 0.0754 | 0.7397 | 0.7267 | 0.7387
Totally 11 treatments with FR at dark period and temperature @ 18 C | 0.0661 | 0.9222 | 0.917 | 0.9157
Groups |  | T-PSS 300~800 nm | T-PSS 600~700 & 700~800 nm | D-PSS
Totally 21 treatments with various dark temp., duration of light period, intensity of CW and FR, FR concurrent with CW or FR in dark period only. | 0.0754 | 0.7397 | 0.7267 | 0.7387
Totally 11 treatments with FR at dark period and temperature @ 18 C | 0.0661 | 0.9222 | 0.917 | 0.9157

## Slide 40
T-PSS 與 D-PSS 存在線性關係
There is a linear relationship between T-PSS and D-PSS
Y = 1.1875 X
R2 = 0.9997

## Slide 41
PSS or PSS x duration or % far red can’t be used to predict flowering ratio
Thermal reversion of phytochrome in dark period should not be neglected in PSS model.
T-PSS and D-PSS can be used to predict flowering ratio.
D-PSS is a simplify T-PSS using only DLI of R and FR instead of spectral data.
Conclusion

## Slide 42
Kalaitzoglou et al., 2019
PSS vs. Photomorphogenesis
Higher PSS, less no. of open flowers on wk 4
less no. of fruits
less % of red fruit
less total fruit weight/plt
small fruit FW
Tomato

## Slide 43
Treatment | T-PSS | D-PSS | Flowering rate
6CW (12)_4FR (2) 25/23℃ | 0.0029 | 0.0034 | 6.67%
6CW (12)_4FR (2) 20/18℃ | 0.0326 | 0.0390 | 6.67%
6CW (12)_4FR (1) 25/23℃ | 0.0030 | 0.0036 | 20.00%
6CW (12)_4FR_half (2) 25/23℃ | 0.0030 | 0.0036 | 26.67%
6CW (12)_2FR (2) 20/18℃ | 0.0333 | 0.0399 | 27.27%
6CW (12)_2FR_diffuse (2) 20/18℃ | 0.0336 | 0.0402 | 27.27%
6CW (12)_4FR (1) 20/18℃ | 0.0340 | 0.0407 | 27.27%
6CW (12)_4FR_half (2) 20/18℃ | 0.0340 | 0.0406 | 36.36%
6CW (13)_4FR (4) 25/18℃ | 0.0398 | 0.0465 | 46.15%
6CW (12) 20/18℃ (CK) | 0.0359 | 0.0430 | 58.33%
6CW (13)_4FR (3) 25/18℃ | 0.0414 | 0.0491 | 64.29%
6CW (13)_4FR (2) 25/18℃ | 0.0429 | 0.0504 | 66.67%
6CW (14)_4FR (3) 20/18℃ | 0.0542 | 0.0644 | 85.00%
6CW (14)_4FR (4) 20/18℃ | 0.0522 | 0.0624 | 90.00%
6CW (14)_4FR (2) 20/18℃ | 0.0557 | 0.0662 | 95.00%
6CW (14)+4FR (2) 20/18℃ | 0.0557 | 0.0664 | 95.00%
6CW (14)+4FR (4) 20/18℃ | 0.0511 | 0.0611 | 100.00%
6CW (14)+4FR (3) 20/18℃ | 0.0527 | 0.0628 | 100.00%
6CW (14)+4FR_half (4) 20/18℃ | 0.0549 | 0.0658 | 100.00%
6CW (14)+4FR_half (3) 20/18℃ | 0.0570 | 0.0675 | 100.00%
6CW (14)+4FR_half (2) 20/18℃ | 0.0584 | 0.0688 | 100.00%
各处理组之兩种修正後光稳态平衡模式与开花率
Two modified photostationary state models and flowering rate of each treatment