## Slide 1: Environmental Control in PFAL Nutrients & Water
Wei FANG
Dept. of Biomechatronics Engineering (BME) and Global ATGS
Center of Excellence for Controlled Environment Agriculture (CCEA)
National Taiwan University (NTU)
[ATGS 7140] Plant Factory – Theory and Practice

## Slide 2
Topic 5
Topic 4
Topic 6

## Slide 3: Five governing factors in PFAL
Air
Light
Water
Nutrient
Gas
Air velocity, Temperature, Relative humidity
quality
Intensity: PPFD
duration
When
Frequency
Dissolved Oxygen
Root zone Temperature
recipe
concentration: EC
Availability: pH
CO2
concentration

## Slide 4: Must have monitoring items in PFAL
Air Light Gas
Water Nutrient
Light Intensity, quality, duration
T、 RH、Wind
CO2
pH、EC
Tw、DO

## Slide 5: Factors affecting plant growth and development
Temperature
Light
Humidity
Nutrient+H2O
Degree of influence: +++ large, ++ medium, + small
Suitable range in between 15 ~ 30 oC
photosynthesis
respiration
Absorb. of nutrient+H2O
Transpiration
Development (leaf,flower formation)
booming
fruiting
Distribution of sugar
Formation of organ
Extension of cell/organ
Mature of fruit
++
Modified by Fang, 2018

## Slide 6
Tair
Tleaf
Resistant of root, root zone
Water potential difference between root and growth media
root
stem
leaf
plant
etc.
Stomata resistant
Air velocity (resistant of boundary layer of air and leaf)
VPD/AHD between air and leaf affected by T and RH / AH
light
H2O CO2 concentration
Energylight (480kJ)
Material exchange: H2O, inorganic macro/micro nutrients (N, P, K, …) concentration
Flower
Fruit
materials
2ndary metabolites

## Slide 7: Outline
Preparation of nutrient solution
pH, EC
Management
pH
Adjustment
Hydroponic systems
Literature Review
Materials / Device
Recipes
Unit conversion
Preparation of nutrient solution
pH, EC
Management
pH
Adjustment
Hydroponic systems
Literature Review
Materials / Device
Recipes
Unit conversion
All about hydroponics
What is hydroponics and how does it works?

## Slide 8: Materials and Device
Mag. mixer/blender
5 L bucket
Micro balance
Fertilizers
Stir bar

## Slide 9: Related Equipment
Balance:
  Micro-elements: 0.001 g grade (precise scale)
  Macro-elements: 0.1 g grade
blender

## Slide 10
Macro elements of Yamazaki formula for various crops
KNO3
Ca(NO3) 2．4H2O
MgSO4．7H2O
Fe．EDTA
EC
NO3-N
K Ca P Mg
PP
NH4 H2PO4
Lettuce
1000 L nutrient solution
Notes: 手調換作物 量大
經驗
STRESS

## Slide 11: Stock solution for micro elements dilute 10,000 times to use
 | concentration | Fertilizer | concentration | Amount required in 10 L of stock solution（g）
 | ppm |  | (mg/L ) | 
B | 0.5 | 硼酸 (H3BO3) | 2.86 | 286
Mn | 0.5 | 氯化錳 (MnCl2．4H2O) or 硫酸錳（MnSO4．4H2O） | 1.81 or 2.13 | 181 or 213
Zn | 0.05 | 硫酸鋅 (ZnSO4．7H2O) | 0.22 | 22
Cu | 0.02 | 硫酸銅 (CuSo4．5H2O) | 0.08 | 8
Mo | 0.01 | 鉬酸鈉 (Na2MoO4．2H2O) | 0.025 | 2.5
Fe | 3 | EDTA-Fe |  | 226
add 0.1 L (100 ml) of stock solution in 1 ton (1000 L) of nutrient solution

## Slide 12: Concentration of recipe
1 S: 1 Strength
½ S: Half Strength
¾ S: 3 quarter Strength
½ or ¾ only represents concentration of macro elements. Concentration of micro elements should remain the same.
Assuming using Yamazaki lettuce formula at 3/2 S, means all the macro elements are 3/2 times of 1 S， EC should be 0.8 x 3/2 = 1.2 mS.cm-1

## Slide 13: Absorption of macro elements of Tomato under various strength of recipe concentration
1 S：N 200, P 31, K 274, Ca 160, Mg 48 ppm
Tomato enjoy K and N
Too much K+ inhibit absorption of Ca+2 and Mg+2

## Slide 14
GROWTH ELEMENT
NO3
Nitrate
NH4
Ammonium
Vegetative Growth Stage

## Slide 15
HEALTH ELEMENT
Heavy Fruiting and
Flowering
Add with
Bloom
Stimulants

## Slide 16: Tomato Recipe

## Slide 17
N
K
Ca
Mg
P
S
BASE NUTRIENTS
Macro nutrients
Macro elements

## Slide 18
Fe
Mn
Cu
Ni
Mo
Cl
Zn
B
Other important trace elements
Micro nutrients
Micro elements
Si

## Slide 19
19 elements for plants |  |  |  | 
類別 | element | Atomic weight | Available form | 
Macro 3 | 碳 C | 12.01 | CO2 | 1mM 44 mg
 | 氫 H | 1.01 | H2O | 1mM 18 mg
 | 氧 O | 16 | O2 | 1mM 32 mg
Macro 6 | 氮 N | 14.01 | NO3-,NH4+ | 1 me = 14.0 mg
 | 磷 P | 30.98 | H2PO4-,HPO4-2 | 10.3
 | 鉀 K | 39.1 | K+ | 39.1
 | 鈣 Ca | 40.08 | Ca+2 | 20
 | 鎂 Mg | 24.32 | Mg+2 | 12.1
 | 硫 S | 32.07 | SO4-2 | 16
Micro 7 | 鐵 Fe | 55.85 | Fe+3,Fe+2 | 27.9
 | 錳 Mn | 54.94 | Mn+2 | 27.5
 | 硼 B | 10.82 | BO3-3,B4O7- | 3.6
 | 銅 Cu | 63.54 | Cu+2,Cu+ | 31.8
 | 鋅 Zn | 65.38 | Zn+2 | 32.7
 | 鉬 Mo | 95.95 | MoO4-2 | 48
 | 氯 Cl | 35.46 | Cl- | 35.4
Special 3 | 矽 Si | 28.09 | SiO4-4 | 7
 | 鋁 Al | 26.98 | Al+3 | 9
 | 鈉 Na | 22.99 | Na+ | 23

## Slide 20: Competition/Cooperation among ions
Ions in same quadrant are competing
Plant preferred ions with low atomic weight x valence
  NH4+>Na+>K+>Mg+2>Ca+2
  18, 23, 39, 24*2, 40*2
ions in different quadrants also affect one another
  Macro affects micro, such as P up, inhibits Fe, Mn, Zn
  Micro affects macro, such as Si, B up, promotes Ca
Cation
Anion
Trace Element
Micro Element

## Slide 21: AEA Antagonistic interactions
www.NovaCropControl.nl
Low K  High Mg  low NO3  high P  low Zn

## Slide 22: Biochemical sequence of nutrition in plants

## Slide 23
Type of fertilizer | Molecular formula | Molecular weight | ion | solubility | purity | Price
 |  |  |  | 20℃ g/l | % | NT$/kg
硝酸鉀 | KNO3 | 101 | K+,NO3- | 315 | 95 | 50~60
硝酸鈣 | Ca(NO3)2‧4H2O | 236 | Ca+2,2(NO3-) | 1270 | 70 | 20~27
磷酸銨 | NH4H2PO4 | 115 | NH4+,H2PO4- | 365 | 98 | 50~64
硫酸鎂 | MgSO4‧7H2O | 246 | Mg+2,SO4-2 | 252 | 45 | 44
硝酸銨 | NH4NO3 | 80 | NH4+,NO3- | 655 | 98 | 
硫銨 | (NH4)2SO4 | 132 | 2(NH4+),SO4-2 | 754 | 94 | 5.6
氯化銨 | NH4Cl | 53 | NH4+,Cl- | 1630 |  | 
尿素 | (NH2)2CO | 60 | NH4+ | 1000 | 98 | 9.8
硫酸鉀 | K2SO4 | 174 | 2K+,SO4- | 111 | 90 | 31
氯化鉀 | KCl | 74 | K+,Cl- | 265 | 95 | 8.4
氯化鈣 | CaCl2‧2H2O | 147 | Ca+2,Cl- | 536 | 75 | 24
磷酸一鉀 | KH2PO4 | 136 | K+,H2PO4- | 227 | 98 | 70
EDTA鐵 | Fe-EDTA | 421 | Fe+2 | 421 | 12.5 | 250
硼酸 | H3BO3 | 62 | B3+ | 46 | 18 | 55~60
硫酸錳 | MnSO4‧4H2O | 223 | Mn+2,SO4-2 | 500 | 99 | 
Frequent used fertilizer

## Slide 24: Nutrient Concentration Frequent used units
Macro elements
    mM 或 mmol/L
    me/L
Micro elements
    ppm
    mg/L
    M 或 mol/L
gram equivalent = atomic weight/valence (克當量=原子量/原子價)
Milligram equivalent, me = e/1000 毫克當量

## Slide 25: me/L to ppm
ppm: parts per million
1 mg in in 1 L of water, 1 g in 1000 L of water
1 g in 1 ton of water is 1 ppm
me/L x atomic weight/valence = ppm
Element | Atomic weight | Valence | 1 me/L
K | 39.1 | 1 | 39.1 mg/L
Ca | 40 | 2 | 20 mg/L
Mg | 24.3 | 2 | 12.15 mg/L

## Slide 26
Example
fertilizer | N |  | P | K | Ca | Mg | EC | Amount
 | NO3-N | NH4-N |  |  |  |  |  | 
unit | me/L | me/L | me/L | me/L | me/L | me/L | mS/cm | g
Target concentration | 7 | 0.67 | 2 | 4 | 3 | 2 | 0.24 | 
Source water | 0 | 0 | 0 | 0.02 | 1.6 | 0.45 |  | 
Required | 7 | 0.67 | 2 | 3.98 | 1.4 | 1.55 |  | 
KNO3 | 3.98 |  |  | 3.98 |  |  |  | 402
Ca(NO3)2．4H2O | 1.4 |  |  |  | 1.4 |  |  | 165
MgSO4．7H2O |  |  |  |  |  | 1.55 |  | 191
NH4H2PO4 |  | 0.67 | 2 |  |  |  |  | 76
(NH4NO3) | (1.62) | (1.62) |  |  |  |  |  | (64.8)
(KNO3) | (1.62) |  |  | (1.62) |  |  |  | (163.6)
合計 | 5.38 | 0.67 | 2 | 4 | 3 | 2 |  | 
3.98 me/L N  3.98 x (39+62) / 1 = 401.98 g KNO3 (KNO3 molecular weight 39+62 )
1.4 me/L Ca  1.4 x (40+62x2+4x18) / 2 = 330/2 = 165

## Slide 27: Yamazaki formula for Lettuce
Chemical composition of nutrient solution. | purity (％) | lettuce (mg/L) | Stock solution (100X) (g/500 mL) | Stock solution (100X) (g/500 mL)
硝酸鈣 Ca(NO3) 2．4H2O | 70 | 240 | 12 | 12/0.7 = 17.14
硝酸鉀 KNO3 | 99.8 | 400 | 20 | 20.04
硫酸鎂 MgSO4．7H2O | 49 | 125 | 6.25 | 12.76
磷酸ㄧ銨 NH4H2PO4 | 98.5 | 60 | 3 | 3.05
鉗形鐵 Fe．EDTA | 99.9 | 20 | 1 | 1.00
硼酸 H3BO3 | 99.9 | 1.2 | 0.6 (1000X；500 mL) | 0.6006
硫酸銅 CuSO4．5H2O | 99.9 | 0.09 | 0.045 (1000X；500 mL) | 0.0450
硫酸鋅 ZnSO4．7H2O | 98 | 0.04 | 0.02 (1000X；500 mL) | 0.0204
硫酸錳 MnSO4．H2O | 97.5 | 1.82 | 0.813 (1000X；500 mL) | 0.8339
鉬酸鈉 NaMoO4．2H2O | 99.9 | 0.01 | 0.005 (1000X；500 mL) | 0.0050
Notes: 12*100/70=17.14

## Slide 28: 2 versions of Yamazaki Recipe
or
or
or
or
or
or
g/5L for stock solution, diluted 200 times, EC = 800 μS/cm = 0.8 mS/cm
Molecular weight
Compound

## Slide 29
diluter

## Slide 31: Commercially available fertilizers for hydroponic systems

## Slide 32
 | N:P:K | 
No.1 | 07-06-19 | Leafy vegetable
No.2 | 20-20-20 | General usage
No.3 | 10-30-20 | Promote flowering
No.4 | 25-05-20 | Leafy Ornamental plants
No.5 | 30-10-10 | Fast growth of Seedling
Hyponex
various size
  Medium: 500 g
  Large: 2 kg, 800 NT$

## Slide 33
Hyponex NO.1 |  |  | 
氮 |  |  | 7%
銨態氮 | Ammoniacal Nitrogen | NH4-N | 1.2%
硝酸態氮 | Nitrate Nitrogen | NO3-N | 5.8%
可利用磷 | Available Phosphate | P2O5 | 6%
水溶性鉀 | Soluble Potassium | K2O | 19%
來源 | Sources |  | 
硝酸鉀 | Potassium Nitrate |  | 
重過磷酸鈣 | Triple SuperPhosphate |  | 
硫酸銨 | Ammonium Sulfate |  | 
Hyponex No.1 (N-P-K: 7-6-19)

## Slide 34: More recipes
Elements | US Hoagland and Arnon / Modified Hogland | UK Cooper | Netherlands Modified Steiner | US Wilcox 1 | US Wilcox 2 | Canada Resh | Japan
N | 210 / 224 | 200 | 171 | 132 | 162 | 175 | 132
P | 31 / 62 | 60 | 48 | 58 | 58 | 65 | 42
K | 234 / 235 | 300 | 304 | 200 | 284 | 400 | 314
Ca | 160 / 160 | 170 | 180 | 136 | 136 | 197 | 162
Mg | 48 / 24 | 50 | 48 | 47 | 47 | 44 | 50
Fe | 50 / 1~3 | 12 | 3 | 4 | 4 | 2 | 3
Mn | 0.5 / 0.11 | 2 | 1 | 0.5 | 0.5 | 0.5 | 0.5
B | 0.5 / 0.27 | 1.5 | 0.3 | 1.5 | 1.5 | 0.5 | 0.5
Zn | 0.05 / 0.13 | 0.1 | 0.4 | 0.3 | 0.3 | 0.05 | 0.05
Cu | 0.02 / 0.03 | 0.1 | 0.2 | 0.1 | 0.1 | 0.05 | 0.02
Mo | 0.01 / 0.05 | 0.2 | 0.1 | 0.1 | 0.1 | 0.02 | 0.01
S | / 32 |  |  |  |  |  | 
Cl, Ni, Si | / 1.77, 0.03, 28 |  |  |  |  |  | 
in ppm

## Slide 35
35
Modified Hoagland
Notes: Ca (uM)=1000000uM *4/1000=4000uM
N (uM)=1000000uM*6/1000+1000000uM*4/1000*2+1000000uM*2/1000=6000+8000+2000=16000
Ca (ppm)=236000mg/L *4/1000*40/236.16=160 N(ppm)=101100mg/L*6/1000*14/101.1+236160*4/1000*14/236.16*2+115080*2/1000*14/115.08=84+112+28=224

## Slide 36
36
Notes: pp4e-table-05-03-2.jpg

## Slide 37
37
Notes: pp4e-table-05-03-3.jpg

## Slide 38: Radish and Lettuce JFK Space Center
0.12 S/m = 1.2 mS/cm = 1200 μS/cm
mM = mmol/L
μM = μmol/L

## Slide 42
Home Hydroponic Garden’s Recipe |  |  |  | 
 | Compound |  | g/10L | 
Stock A | 磷酸一銨 | NH4H2PO4 | 340 | 
(Macro) | 硝酸鈣 | Ca(NO3)2．4H2O | 2080 | 
 | 硝酸鉀 | KNO3 | 1100 | 
 |  |  | g/4L | 
Stock B | 硫酸鎂 | MgSO4‧7H2O | 492 | 
(Micro) | 硫酸錳 | MnSO4．4H2O | 2.48 | 
 | 硼酸 | H3BO3 | 6.2 | 
 | 硫酸銅 | CuSO4．5H2O | 0.48 | 
 | 硫酸鋅 | ZnSO4．7H2O | 1.2 | 
 | 鉬酸銨 | (NH4)6Mo7O24．4H2O | 0.02 | 
 | 螯合鐵 | EDTA2Fe | 8.46 | 
add 5 ml A(Macro) and 2 ml B(micro) in 1 L of water |  |  |  | 
Bradley, P. And Tabares, C.H.M., 2000, Spreading Simplified Hydroponics：Home Hydroponic Gardens, Global Hydroponics Network, Corvallis, OR. |  |  |  | 

## Slide 43
Generic Hydroponic Recipe |  |  | 
 | Compound |  | g/100L
A | 硝酸鈣 | Ca(NO3)2．4H2O | 13110
 | 硝酸鉀 | KNO3 | 2557
 | 螯合鐵 | EDTA2Fe | 500
B | 硝酸鉀 | KNO3 | 2557
 | 磷酸鉀 | KH2PO4 | 3567
 | 硫酸鎂 | MgSO4‧7H2O | 6625
 | 硫酸錳 | MnSO4．4H2O | 121
 | 硫酸鋅 | ZnSO4．7H2O | 11
 | 硼酸 | H3BO3 | 39
 | 硫酸銅 | CuSO4．5H2O | 3
 | 鉬酸銨 | (NH4)6Mo7O24．4H2O | 1.02
Both dilute 1: 100, EC=2.5, TDS=1806 |  |  | 
Morgan, L., 2002e, The Growing Edge 14(1)：11. |  |  | 

## Slide 44: Lettuce (for 300 L RO water)
diluted 100 times for plants
Both ends of red line will leads to precipitation if put in same tank
Stock A and B should not mixed directly, dilute separately
Cornell Univ.

## Slide 45: for 30 L RO water

## Slide 46: 4 single element fertilizers for stock solution A
四水硝酸鈣
硝酸鉀
硝酸銨
螯合鐵

## Slide 47: 4 out of 9 single element fertilizers for stock solution B
硝酸鉀
KNO3
磷酸一鉀
KH2PO4
硫酸鉀
K2SO4
MgSO4.7H2O
七水硫酸鎂

## Slide 48: 5 out of 9 single element fertilizers for stock solution B
一水硫酸亞錳 硼酸 五水硫酸銅 二水鉬酸鈉 七水硫酸鋅
Zinc Sulfate*7H2O (??%Zn)

## Slide 49: Final concentration of each element
millimol/L * molecular weight = mg/L = ppm
micromol/L * molecular weight / 1000 = ppm
14
31
39
40
24
32

## Slide 50
2015 Cornell Recipe：DFT
For 100 gallon (378.5 L) RO water = Dilute 100 times in 1 gallon RO water to make stock solution
4
7
New recipe
Old recipe
9
4

## Slide 51: Comparison on new/old Cornell Recipes
4
7
4
9

## Slide 52: 2015 Cornell
Recipe adjustment due to compounds with various hydrate
or
or
or
Magnesium sulfate heptahydrate
Magnesium sulfate monohydrate
Magnesium sulfate

## Slide 53: Outline
Preparation of nutrient solution
pH, EC
Management
pH
Adjustment
Hydroponic systems
Literature Review
meters
Introducing EC & pH
Maintenance of electrodes
EC control

## Slide 54
Desktop device
EC meter pH meter

## Slide 55: Portable pH/EC meter

## Slide 56: pH and Alkalinity

## Slide 58: Alkalinity
Alkalinity: Determine the sensitivity / durability of water to pH variation.
Low alkalinity: very sensitive
High alkalinity: low sensitive, required more acid to reduce pH and more alkali liquid to increase pH
Alkalinity high, pH also high
Knowing alkalinity of source water is vital.
Alkalinity test strip

## Slide 59: Proper range for alkalinity

## Slide 60: Electrical Conductivity (EC)
Positively proportion to concentration of ionized nutrients
EC in mS/cm= mmhos/cm
    1.0 mS/cm = 0.1 S/m = 1000 S/cm
    1 dS/m = 0.1 S/m = 100 mS/100 cm = 1 mS/cm
An overall index, not able to know details of each elements
EC meter
solution
electrod
electrod
Notes: ++++++++

## Slide 61: Electrical Conductivity (EC)
?
Lots of Units
1 mS/cm
1 dS/m
1 mmhos/cm
1000 μS/cm
1000 μmhos/cm

## Slide 62: RO water is a must better source water
Assuming Target EC for nutrient solution is 1.2 mS/cm
Water | EC mS/cm | Unknown risk | 
Tap water | 0.2 | 16.67% | 20
Tap water | 0.1 | 8.3% | 10
RO water | 0.01 | 0.83% | 1

## Slide 63: Upper limit of source water

## Slide 64
EC vs. Nutrient concentration of a Japanese hydroponic recipe

## Slide 65: EC, CF, TDS
More ions in the water leads to higher Electrical Conductivity.
Three commonly used terms for measuring concentration of the solution：
  EC (in mS/cm or μS/cm)、 Conductivity Factor (CF, in CF) and Total Dissolved Solid (TDS, in ppm)
    Convert EC to CF: 1 mS/cm = 10 CF
    Convert EC to TDS: There exists different standard, leads to different conversion constant. 1 mS/cm = 500, 640 and 700 ppm for US、ERUO and Australia, respectively.

## Slide 66
Conversion Tables for devices from different countries
for EC measurement

## Slide 67: pH
Range of pH varied for different crops
pH range for hydroponics: 5.5~6.5

## Slide 68
pH > 8
pH < 4.5

## Slide 69: pH Adjustment for RO/Tap water
RO water | 
pH | 5.0~5.3~5.5
EC | < 0.01 mS/cm
Tap water in Taipei | 
pH | 6.4~6.5~6.6
EC | 0.1 mS/cm
Target pH for hydroponics 5.5~6.5 | 
RO water need to add NaOH or KOH Tap water need to add H3PO4 or HCl or H2SO4 | 

## Slide 70: portable pH meter

## Slide 71: Maintenance of electrodes
pH & EC electrodes are consumable materials
  Both required calibration at least once per month.
  EC electrode has min maintenance requirement
  pH electrode
    has short usable lifespan (6 ~ 12 months)
    need to be submerged in saturated KCl solution when not in use.

## Slide 72: EC calibration solution
If provided is powder type, need to be soak in pure water or at least de-ionized water to make the calibration solution
EC calibration solution has sever standards (upper photo)
Commonly used is under 25 oC, EC values of 1413 and 12880 S/cm
Solution at different temperature will have different EC value ever for same standard solution. (as shown in the bottom photo)

## Slide 73: pH buffer solution
pH buffer solution is in liquid form
  normally pH = 4, 7, 10
  Temperature also affects pH values, as shown below pH = 10.01
For hydroponic applications, only pH=4, 7 are needed for calibration.

## Slide 74: EC control
EC low, provide with rich solution
  Manually
  Direct injection
  Using Solenoid Valves
  Using peristaltic pump
EC high, add in RO water
  Manually
  Automatically (water level valve)

## Slide 75: Direct injection
pH, EC and water temperature sensors

## Slide 76: Solenoid Valves

## Slide 77: peristaltic pump

## Slide 78: Design 1: sensors in the buffering tank
Controller
EC sensor
pH sensor
fixed amount
peristaltic pump
To growth area
circulation
pump
acid
A solution
B solution
peristaltic pump

## Slide 79: Design 2：Sensors not in the buffering tank

## Slide 80: Two water levels to control EC

## Slide 81
Control box
Touch screen

## Slide 82: Example of a pH, EC control Box

## Slide 83: Concentrated Tanks
30 L PE buckets/tanks for concentrated A, B solutions
Float valve

## Slide 84: Mixing tank
Nutrient supply line

## Slide 85
Nutrient control
Kong and Fang, 2012
Two water levels control
return water inlet
water outlet

## Slide 86
EC control (60 L water)
EC Set point：1200 S/cm
Time elapsed, min
EC from 1000  1200 S/cm
  required < 2 min

## Slide 87
pH control (60 L water)
pH setpoint：5.5
Time elapsed, min
pH from pH = 5  5.5
  required 2.5 min

## Slide 88
Apply this system to 6 ton of water
EC from 1000  1200 S/cm
  required 2 x (6000/60) = 200 min (1 S/cm / min)
pH from pH = 5  5.5
  required 2.5 x 100= 250 min (0.01 / 5 min)
Capability of the control > dynamic change of the culturing system

## Slide 89: Variation of EC 0 ~ 10 g/L of Hyponex No.1

## Slide 90: Variation of EC 0 ~ 1 g/L of Hyponex No.1

## Slide 91
Variation of EC 0 ~ 10 g/L of Hyponex No.2

## Slide 92
Variation of EC 0 ~ 3 g/L of Hyponex No.2

## Slide 93
Variation of EC 0 ~ 2 g/L of Hyponex No.2

## Slide 94: Hyponex No.1 vs. No.2
Required quantity, no. of 2 kg boxes and total price
for 1 ton of nutrient solution@ EC=1.2 mS/cm
boxes
total NT$
No.1
No.2
No.1
No.2
= (1.2 – 0.01)/1.152
= (1.2 – 0.01)/0.892
Assuming 800 NT$ per 2 kg pack

## Slide 95: Outline
Preparation of nutrient solution
pH, EC
Management
pH Adjustment
Hydroponic systems
Literature Review

## Slide 96: Variation of pH 0 ~ 1 g/L of Hyponex No.1

## Slide 97: Variation of pH 0 ~ 1 g/L of Hyponex No.2

## Slide 98: pH variation in Hyponex No.1, 2
Hyponex No.1
Hyponex No. 2
N:P:K
07-06-19
N:P:K
20-20-20
K+  H+
NO3-  OH-

## Slide 99: pH variation of 0 ~ 30 g/L Hyponex No.2
Not totally dissolved

## Slide 100: pH variation of 0 ~ 8 g/L Hyponex No.2
Not totally dissolved

## Slide 101: Range of pH for hydroponic system
pH range
  Best: 6.0~6.2
  Proper: 6.0-6.5
  OK: 5.5-6.5
  pH > 8, Fe, Mn, P deficit
  pH < 4.5, Ca, Mg, K precipitation and more

## Slide 102: pH affects availability

## Slide 103: A different diagram proper range: 6.5~7 for soil

## Slide 104
1000 L target pH6.0 H3PO4 (mL) |  |  | 1000 L target pH6.0 KOH (mL) | 
pH | 8.5% H3PO4 |  | pH | 4.0% KOH
7.0 | 940.7 |  | 5 | 707.9
6.9 | 891.7 |  | 5.1 | 666.8
6.8 | 832.7 |  | 5.2 | 619.2
6.7 | 763.7 |  | 5.3 | 564.9
6.6 | 684.6 |  | 5.4 | 504
6.5 | 595.6 |  | 5.5 | 436.5
6.4 | 496.5 |  | 5.6 | 362.5
6.3 | 387.4 |  | 5.7 | 281.8
6.2 | 268.3 |  | 5.8 | 194.4
6.1 | 139.1 |  | 5.9 | 100.5
6.0 | – |  | 6 | –
pH adjustment

## Slide 105: pH adjustment pH DOWN
T affects pH
Same amount of acid does not bring down same amount of decrease in pH

## Slide 106: pH adjustment pH UP
T affects pH
Same amount of alkali liquid does not leads to same amount of pH increment
pH adjustment is more difficult to predict compare with EC adjustment

## Slide 107: Reduce pH

## Slide 108: Amount of pH decrement

## Slide 109: Increase pH

## Slide 110: Amount of pH increment

## Slide 111: pH adjustment
To reduce pH by 1, such as pH 7  pH 6
  Required 0.9~1 ml/L of 8.5%H3PO4
  Diluted 200 times first then drip in and stirred
To increase pH by 1, such as pH 5  pH 6
  Add 0.7 mL/L of 4 %KOH
  Diluted 200 times first then drip in and stirred
The variation of pH is not linear to the amount of H3PO4 or KOH added.

## Slide 112: Reasons of pH variation during cultural period
Plant absorption differences among elements, such as tomato prefer NO3-，PO3-3 and K+, melon prefer Ca+2 and Mg+2
Improper match of recipe and plants
Under strong light and high T, plants absorbed more N, P, K, absorbed less Ca, Mg, leads to pH increase
Under less light and low T environment, pH tends decrease

## Slide 113: Reasons of pH variation during cultural period (cont..)
CO2 in the air dissolved in water to form H2CO3 (carbonic acid), leads to pH decrease
from respiration of root, CO2 combined with Ca+2、Mg+2 to form CaCO3, MgCO3 precipitation, lead to increase of pH
Some plants such as lettuce, strawberry preferred NH4+(Ammonium), after absorption, roots excrete H+ leads to reduction of pH
Some plants such as pak choy, Chinese cabbage preferred NO3- (Nitrate), after absorption, roots excrete OH- leads to increase of pH

## Slide 114: pH variation after root absorbed NH4+/NO3-
NH4+
NO3-

## Slide 115: Outline
Preparation of nutrient solution
pH, EC
Management
pH adjustment
Hydroponic systems

## Slide 116: Comparison on 4 hydroponic systems
1
2
3
4
NFT
DFT/DWC with air pump
DFT/DWC without air pump
DFT/DWC with capillary stripe
Wick culture

## Slide 117: Comparison on 4 hydroponic systems
Pak choy
Lettuce
Bok choy
1 2 3 4
1 2 3 4
1 2 3 4
1 2 3 4
Scallion

## Slide 118: Popular Hydroponic Systems
Nutrient Film Technique, NFT Leafy vegetable (UK)
Deep Flow Technique, DFT Deep Water Culture, DWC Leafy vegetable (Japan)
Drip Irrigation (rockwool) Vine plants: tomato, melon, pepper, cucumber (The Netherlands)
Ebb and Flow (E&F)
all of above, tuber plant
Aeroponics (spraying, misting, fogging)
Wick culture

## Slide 119: NFT
Easy installation
Low installation cost
Continuous flow
Advantages of NFT

## Slide 120: NFT trough system

## Slide 121: Disadvantages of NFT
Limited amount of nutrient solution
  Large influence by the surrounding temperature due to high water T has low saturated dissolved oxygen (DO). only true for GH, not for PFAL
  Large influence by the plant absorption
Limited space for root growth: only suitable for plants that did not has lots of roots
Vigorous growth of root might block the solution flow leads to uneven distribution of nutrient concentration
Easy to fail in in locations with unstable power supply

## Slide 122: DFT / DWC

## Slide 123: DFT: Pipe Culture

## Slide 125: DFT bench system

## Slide 126: Hyponica style DFT
M style DFT

## Slide 127
Fixed platform DFT without air pump
Roots are partially soaked in nutrient solution

## Slide 128
Floating platform DFT with air pump
Roots are totally soaked in nutrient solution

## Slide 129: Disadvantages/Advantage of DFT
Compare with NFT
  More solution required
  More nutrients required
  DO is of great concerned
  More costly to setup and to operate
  Easy to manage, for beginners
  Limited variation on DO due to air T
  Limited variation on nutrients due to plant absorption

## Slide 130: Drip irrigation using rockwool

## Slide 131: Rockwool cube and plate
Rockwool cube
Rockwool plate

## Slide 132: Drip irrigation using rockwool High wire system

## Slide 133: Various Systems using Rockwool
Drip irrigation
Ebb and Flow

## Slide 134: Ebb and Flow using double pumps
Pump 1 & Pump 2 switch on/off
Pump1
Pump2

## Slide 135: Amount of water used
NFT < E&F < DFT
Little water used, no room for error, less forgiving
More water used, more fertilizer required, higher operating cost
More water used, heavier the static load to the growth shelf, higher hardware fixed cost

## Slide 136: Aeroponics

## Slide 138: Aeroponics

## Slide 140
Tuber plants
Potato
Sweetpotato
Jingsung

## Slide 141: TS type PFAL: Aeroponics T: triangle, S: spray

## Slide 142: TS 700 and TS 1000
1993, Kyoto, Japan
400 m2
Production 700 plant/day (TS700)
4 employee
2001, Kyoto, Japan
500 m2
Production 1000 plant/day (TS1000)
6 employee

## Slide 143
HPS lamp
TS type PFAL: Aeroponics

## Slide 144: Aeroponics

## Slide 145
https://youtu.be/YDQQj-WzT_U
https://www.youtube.com/watch?v=ME_rprRlmMM&t=32s
https://www.youtube.com/watch?v=1m9U-AZ98_k
AeroFarms: The largest PFAL in US

## Slide 146: Ratio of nutrient solutions
R = U : B
U: total amount of solution on cultural shelf
B: amount of solution in buffering tank
R small, easy to operate, but required large buffering tank
Manually operated system, R should be minimized
Automatic control system, R should be maximized

## Slide 147: Circulation control
Continuous type
  NFT (Nutrient Film Technique)
  DFT (Deep Flow Technique, also named DWC, deep water culture)
Intermittent type
  Ebb and Flow type
  Aeroponic type
  DFT (DWC)

## Slide 148: Timer for continuous or intermittent control of pump

## Slide 149: Plumbing Design of circulating pumps
Sensor required flowing solution
Buffer tank required stir/Agitating all the time to ensure better mixing and proper DO
149
For Intermittent flow
For Continuous flow

## Slide 150: Outline
Preparation of nutrient solution
pH, EC
Management
pH adjustment
Hydroponic systems
Literature Review

## Slide 151: Literature Review
Influence of sources of N
Influence of NO3/NH4
Influence of water temperature
Influence of concentration of K+
Growing Komatsuna with supplemental micro elements

## Slide 152
L1. Hoagland for lettuce - With different source of N
Compound | Concentration of stock | Final concentration of element (ppm) | 
Potassium nitrate (NO3-) or ammonium sulfate (NH4+) or potassium nitrite (NO2-) |  | N | 50
Potassium sulfate (K2SO4) | 0.25 M | K | 226
Magnesium sulfate (MgSO4) | 0.5 M | Mg | 120
Calcium phosphate [Ca (H2PO4)2] | 0.025 M | Ca | 58
Calcium sulfate (CaSO4) | 0.005 M | Ca | 136
Boric acid (H3BO3) | 0.005 M | B | 0.25
Manganese sulfate (MnSO4) | 0.005 M | Mn | 0.25
Zinc sulfate (ZnSO4) | 0.005 M | Zn | 0.025
Copper sulfate (CuSO4) | 0.005 M |  | 
Sodium molybdate (NaMoO3) | 0.005 M |  | 
pH=6.0~6.5
Communications in Soil Science and Plant Analysis, 2008, 39: 207–216

## Slide 153
Measurements | Sources of N |  | 
 | NO3 | NO2 | NH4
Plant height (cm) | 14.2 a | 12.6 b | 12.8 b
Number of leaves/plant | 9.4 a | 7.4 c | 8.4 b
Root vascular Discolorationa | 0.4 b | 1.6 a | 1.4 a
Root fresh wt (g) | 8.1 a | 4.5 b | 5.0 b
Leaf fresh wt (g) | 46.1 a | 35.6 b | 39.2ab
Fresh biomass yield (g) | 54.2 a | 40.1 b | 44.2 ab
Dry biomass yield (g) | 6.6 | 4.5 | 5.0
Plant NO3-N (mg kg-1) | 3453 a | 3030 a | 2100 b
Table 1. Influence of sources of N and type of lettuce on different attributes of lettuce
aRoot vascular discoloration, rated as 1=low, 2=medium, and 3=high.
Note. Means in the same row followed by different letters are significantly different at the P<0.05 level.
Ns=nonsignificant; , indicate significance at P <0.05 and 0.01 levels, respectively.
Communications in Soil Science and Plant Analysis, 2008, 39: 207–216
L1. Hoagland for lettuce - With different source of N

## Slide 154
L2. Influence of NO3/NH4 ratio on plant height. leaves number, leaf area, yield and RCC of Spinach
Acta Hort. 2009. 843: 269–274

## Slide 155
L3. Water Temperature affects leaf number and length of Spinach
African Journal of Agricultural Research (2009) 4 (12): 1442 - 1446

## Slide 156
African Journal of Agricultural Research (2009) 4 (12): 1442 - 1446
L3. Water Temperature affects yield of Spinach

## Slide 157
Element (mM) | 1/1K | 1/2K | 1/4K | 1/8K | 1/16K
K | 3.000 | 1.500 | 0.750 | 0.375 | 0.188
Ca | 2.000 | 2.750 | 3.125 | 3.313 | 3.406
N | 7.500 | 7.500 | 7.500 | 7.500 | 7.500
NO3-N | 7.000 | 7.000 | 7.000 | 7.000 | 7.000
NH4-N | 0.500 | 0.500 | 0.500 | 0.500 | 0.500
P | 0.500 | 0.500 | 0.500 | 0.500 | 0.500
Mg | 1.000 | 1.000 | 1.000 | 1.000 | 1.000
S | 1.000 | 1.000 | 1.000 | 1.000 | 1.000
Fe | 0.02600 | 0.02600 | 0.02600 | 0.02600 | 0.02600
Mn | 0.00460 | 0.00460 | 0.00460 | 0.00460 | 0.00460
Zn | 0.00038 | 0.00038 | 0.00038 | 0.00038 | 0.00038
Cu | 0.00016 | 0.00016 | 0.00016 | 0.00016 | 0.00016
B | 0.024000 | 0.024000 | 0.024000 | 0.024000 | 0.024000
Mo | 0.00011 | 0.00011 | 0.00011 | 0.00011 | 0.00011
Na | 0.05200 | 0.05200 | 0.05200 | 0.05200 | 0.05200
L4. Concentrations (in mM) of elements in nutrient solution for 5 treatments

## Slide 158: L4. Lower K+ in solution leads to higher Ca+2 and lower Mg+2 in leaves

## Slide 159: Results of above 4 papers
Influence of sources of N for lettuce
  NO3 > NH4 > NO2
Influence of NO3/NH4 for spinach
  75/25 > 50/50 > 25/75 > 100/0
Influence of water temperature for spinach
  28 oC > 26 > 24 ~ 10 oC
Influence of concentration of K+
  Lower concentration of K+ leads to higher Ca+2 and lower Mg+2

## Slide 160
Micro-elements of NTU solution (mg L-1) in EXP 1 |  |  |  |  |  |  | 
Treatments | Fe | Mn | B | Cu | Zn | Mo | Na
NTU (CK) | 3.2 | 0.5 | 0.52 | 0.02 | 0.05 | 0.01 | 1.31
NTU + Mn |  | 1 |  |  |  | 0.01 | 
NTU + Mo |  | 0.5 |  |  |  | 0.45 | 
NTU + MnMo |  | 1 |  |  |  | 0.45 | 
Macro-elements of NTU solution NO3-N:83.9 NH4-N:7.3 PO4-P:16.6 K:154.8 Ca:40.7 Mg:16.6 SO4-S:16.6 |  |  |  |  |  |  | 
L5. Growing Komatsuna with supplemental Micro elements
Aiming at reducing nitrate concentration with no sacrifice on shoot fresh mass
Huang, 2021 (Thesis)

## Slide 161
Treatment code of EXP1 | LED light | Recipe code
CW_NTU (CK) | CW | NTU
CW_NTU + Mn |  | NTU + Mn
CW_NTU + Mo |  | NTU + Mo
CW_NTU + MnMo |  | NTU + MnMo
RW_NTU | RW | NTU
RW_NTU + Mn |  | NTU + Mn
RW_NTU + Mo |  | NTU + Mo
RW_NTU + MnMo |  | NTU + MnMo
LED type | Blue (%) | Green (%) | Red (%) | PPFD (μmol m-2 s-1 )
CW | 27 | 48 | 25 | 236
RW | 1 | 4 | 95 | 232

## Slide 162
Treatment code of EXP1 | Seedling stage (DAS = 8~14) |  | Mature stage (DAS = 15~28) | 
CW_NTU (CK) | L1_236_H24_d182_A25_ | N1_E1.2 | L1_236_H16_d47_A25/20_ | N1_E0.6
CW_NTU + Mn |  | N2_E1.2 |  | N2_E0.6
CW_NTU + Mo |  | N3_E1.2 |  | N3_E0.6
CW_NTU + MnMo |  | N4_E1.2 |  | N4_E0.6
RW_NTU | L2_232_H24_d182_A25_ | N1_E1.2 | L2_232_H16_d47_A25/20_ | N1_E0.6
RW_NTU + Mn |  | N2_E1.2 |  | N2_E0.6
RW_NTU + Mo |  | N3_E1.2 |  | N3_E0.6
RW_NTU + MnMo |  | N4_E1.2 |  | N4_E0.6
Nx：N: Nutrient recipe,
x: type, x=0, tap water, x=1, NTU formula, x=2, NTU + Mn, x=3, NTU + Mo, x=4, NTU + MnMo
DAS=0： H0_N0_E0_ A25
Stage 1 (DAS=1~3)： L1_230_H24_d772_N0_E0 _ A25
Stage 2 (DAS=4~7)： L1_230_H24_d772_N1_E1.2_ A25
Seedling stage (DAS = 8~14) ： Lx_y_H24_d182_Nx_E1.2_A25
Mature stage (DAS = 15~28) ：Lx_y_H16_d47_Nx_E0.6_A25/20
Lx_y：L：LED type，x=1：CW，x=2：RW， y：PPFD in μmol·m-2·s-1
Hx：H: Light period, x：hrs, in h d-1
dx：d: cropping density, x：density in plt·m-2
Ex：E: EC of nutrient solution, x: EC value in mS·cm-1
Ax/y：A: Indoor temperature, x/y: day/night temperature in ℃

## Slide 163
DAS = 28

## Slide 164
Treatment code of EXP1 | Shoot fresh mass (g·plt-1) |  | Nitrate concentration (mg·kg-1)
CW_NTU (CK) | 78.5 ± 20.3 | ab | 7268 ± 717 ab
CW_NTU + Mn | 81.6 ± 18.1 | ab | 8003 ± 541 ab
CW_NTU + Mo | 90.0 ± 16.4 | ab | 8336 ± 1003 ab
CW_NTU + MnMo | 72.0 ± 21.4 | b | 7913 ± 295 ab
RW_NTU | 88.0 ± 28.4 | ab | 6777 ± 703 c
RW_NTU + Mn | 75.5 ± 31.7 | ab | 7113 ± 975 abc
RW_NTU + Mo | 107.9 ± 38.0 | a | 7503 ± 1141 bc
RW_NTU + MnMo | 71.9 ± 25.7 | b | 7794 ± 478 ab
DAS = 28
NTU + Mo is the best recipe for shoot fresh mass
NTU + MnMo leads to biological disorder
High proportion of red light can be used
EC drop from 1.2 to 0.6 at 2 weeks before harvest does not help in reducing nitrate concentration, which is still very high (>> 3000 ppm)
Drop of EC leads to the low shoot fresh mass.

## Slide 165
Treatments of EC reduction at various stages (EC in mS·cm-1) in EXP2 |  |  |  | 
EC reduction code | Seeding stage DAS = 4~7 | Seedling stage DAS = 8~14 | Mature stage 1 DAS = 15~21 | Mature stage 2 DAS = 22~28
EC-48 (no drop) | 1.2 | 1.2 | 1.2 | 1.2
EC-39 (1 rapid drop) | 1.2 | 1.2 | 1.2 | 0.3
EC-36 (1 mild drop) | 1.2 | 1.2 | 0.6 | 0.6
EC-33 (2 mild drops) | 1.2 | 1.2 | 0.6 | 0.3
EC-24 (2 mild drops) | 1.2 | 0.6 | 0.3 | 0.3
L5. Growing Komatsuna with supplemental Micro elements
Aiming at reducing nitrate concentration with no sacrifice on shoot fresh mass

## Slide 166
Treatment code of EXP2 | Recipe | LED | EC reduction code
CW_EC-48 | NTU + Fe | CW | EC-48
CW_EC-39 |  |  | EC-39
CW_EC-36 |  |  | EC-36
CW_EC-33 |  |  | EC-33
CW_EC-24 |  |  | EC-24
R_EC-48 |  | R | EC-48
R_EC-39 |  |  | EC-39
R_EC-36 |  |  | EC-36
R_EC-33 |  |  | EC-33
R_EC-24 |  |  | EC-24
L5. Growing Komatsuna with supplemental Micro elements
Aiming at reducing nitrate concentration with no sacrifice on shoot fresh mass

## Slide 167
Code of EXP2 | Seedling stage (DAS = 8~14) |  | Mature stage 1 (DAS = 15~21) |  | Mature stage 2 (DAS = 22~28) | 
CW_EC-48 | L1_248_H24_d182_A25/20_ | E1.2 | L1_248_H16_d47_A25/20_ | E1.2 | L1_248_H16_d47_A25/20_ | E1.2
CW_EC-39 |  | E1.2 |  | E1.2 |  | E0.3
CW_EC-36 |  | E1.2 |  | E0.6 |  | E0.6
CW_EC-33 |  | E1.2 |  | E0.6 |  | E0.3
CW_EC-24 |  | E0.6 |  | E0.3 |  | E0.3
R_EC-48 | L2_245_H24_d182_A25/20_ | E1.2 | L2_245_H16_d47_A25/20_ | E1.2 | L2_245_H16_d47_A25/20_ | E1.2
R_EC-39 |  | E1.2 |  | E1.2 |  | E0.3
R_EC-36 |  | E1.2 |  | E0.6 |  | E0.6
R_EC-33 |  | E1.2 |  | E0.6 |  | E0.3
R_EC-24 |  | E0.6 |  | E0.3 |  | E0.3
Nutrient recipe is NTU + Fe for all treatments
L5. Growing Komatsuna with supplemental Micro elements
Aiming at reducing nitrate concentration with no sacrifice on shoot fresh mass

## Slide 168
Treatment code of EXP2 | Shoot fresh mass (g·plt-1) |  | Root fresh mass (g·plt-1) | Nitrate concentration (mg·kg-1)
CW_EC-48 | 157.3 ± 37.2 | a x | 16.3 ± 3.8 a | 6193 ± 691 b
CW_EC-39 | 149.6 ± 33.5 | ab | 10.1 ± 3.9 cd | 4846 ± 535 d
CW_EC-36 | 154.7 ± 16.1 | a | 13.0 ± 3.9 b | 5357 ± 622 cd
CW_EC-33 | 140.4 ± 6.5 | abc | 12.9 ± 0.9 bc | 2271 ± 260 e
CW_EC-24 | 82.7 ± 7.7 | d | 10.9 ± 1.7 bcd | 2798 ± 151 e
R_EC-48 | 144.2 ± 6.8 | abc | 10.1 ± 0.6 cd | 7935 ± 688 a
R_EC-39 | 126.1 ± 9.2 | b | 9.4 ± 1.9 d | 5782 ± 846 bc
R_EC-36 | 133.1 ± 17.6 | bc | 10.3 ± 2.3 bcd | 5054 ± 512 d
R_EC-33 | 124.4 ± 5.4 | b | 11.5 ± 0.7 bcd | 2669 ± 362 e
R_EC-24 | 80.9 ± 10.8 | d | 10.4 ± 1.0 bcd | 2261 ± 394 e
Shoot fresh mass (FM) is in direct proportion with total EC CW is better than pure R in shoot fresh mass production using NTU+Fe recipe 4 out of 10 treatments (CW or R_EC-33 and EC-24) have nitrate concentration less than 3000 ppm EC-24 (1.2-0.6-0.3-0.3) treatments have least amount of fresh mass, 2 weeks of EC 0.3 reduced fresh mass a lot. CW_EC-33 (1.2-1.2-0.6-0.3) is the best treatment with shoot FM > 140 g, Nitrate < 3000 ppm). |  |  |  | 
DAS = 28
L5. Growing Komatsuna with supplemental Micro elements
Aiming at reducing nitrate concentration with no sacrifice on shoot fresh mass

## Slide 169
Micro-elements of NTU solution (mg L-1) in EXP3 |  |  |  |  |  |  | 
Treatments | Fe | Mn | B | Cu | Zn | Mo | Na
NTU | 3.2 | 0.5 | 0.52 | 0.02 | 0.05 | 0.01 | 1.31
NTU + Mo | 3.2 |  |  |  |  | 0.45 | 1.31
NTU + Fe | 4.8 |  |  |  |  | 0.01 | 2.06
NTU + MoFe | 4.8 |  |  |  |  | 0.45 | 2.06
LED type | Blue (%) | Green (%) | Red (%) | PPFD (μmol m-2 s-1 )
CW | 27 | 48 | 25 | 248
R | 0 | 0 | 100 | 245
L5. Growing Komatsuna with supplemental Micro elements
Aiming at reducing nitrate concentration with no sacrifice on shoot fresh mass

## Slide 170
Nx：Nutrient recipe type
x=0, tap water, x=1: NTU formula, x=2, NTU+Mo, x=3, NTU+Fe, x=4, NTU+MoFe
Treatments | Seedling stage (DAS = 8~14) |  | Mature stage 1 (DAS = 15~21) |  | Mature satge 2 (DAS = 22~28) | 
CW_NTU (CK) | L1_248_H24_d182_A25_ | N1_E1.2 | L1_248_H16_d47_A25/20_ | N1_E0.6 | L1_248_H16_d47_A25/20_ | N1_E0.3
CW_NTU + Mo |  | N2_E1.2 |  | N2_E0.6 |  | N2_E0.3
CW_NTU + Fe |  | N3_E1.2 |  | N3_E0.6 |  | N3_E0.3
CW_NTU + MoFe |  | N4_E1.2 |  | N4_E0.6 |  | N4_E0.3
R_NTU | L2_245_H24_d182_A25_ | N1_E1.2 | L2_245_H16_d47_A25/20_ | N1_E0.6 | L2_245_H16_d47_A25/20_ | N1_E0.3
R_NTU + Mo |  | N2_E1.2 |  | N2_E0.6 |  | N2_E0.3
R_NTU + Fe |  | N3_E1.2 |  | N3_E0.6 |  | N3_E0.3
R_NTU + MoFe |  | N4_E1.2 |  | N4_E0.6 |  | N4_E0.3
Treatment codes of EXP3 | LED type | Nutrient Recipe
CW_NTU (CK) | CW | NTU
CW_NTU + Mo |  | NTU + Mo
CW_NTU + Fe |  | NTU + Fe
CW_NTU + MoFe |  | NTU + MoFe
R_NTU | R | NTU
R_NTU + Mo |  | NTU + Mo
R_NTU + Fe |  | NTU + Fe
R_NTU + MoFe |  | NTU + MoFe

## Slide 171
DAS = 28

## Slide 172
DAS = 28
Treatment code of EXP3 | Shoot fresh mass (g·plt-1) | Root Fresh mass (g·plt-1) | Nitrate concentration (mg·kg-1)
CW_NTU (CK) | 159.1 ± 8.3 a x | 21.6 ± 1.2 abc | 3013 ± 542 a
CW_NTU + Mo | 155.5 ± 6.9 ab | 21.9 ± 2.6 abc | 2265 ± 291 c
CW_NTU + Fe | 165.2 ± 7.7 a | 23.1 ± 1.6 abc | 2271 ± 260 c
CW_NTU + MoFe | 129.3 ± 13.1 e | 22.0 ± 2.4 abc | 2977 ± 607 a
R_NTU | 139.8 ± 9.0 bc | 22.7 ± 1.9 ab | 2747 ± 496 abc
R_NTU + Mo | 135.5 ± 8.9 de | 19.8 ± 1.6 cd | 2395 ± 400 bc
R_NTU + Fe | 146.4 ± 6.4 bcd | 20.5 ± 1.3 bcd | 2669 ± 362 abc
R_NTU + MoFe | 133.5 ± 9.7 de | 19.1 ± 2.8 d | 2972 ± 508 ab
7 out of 8 treatments, Nitrate concentration < 3000 ppm CW is better than just R NTU+Fe is better than NTU+Mo |  |  | 
L5. Growing Komatsuna with supplemental Micro elements
Aiming at reducing nitrate concentration with no sacrifice on shoot fresh mass

## Slide 173: Hydroponics is a perfect tool for nutrient deficiency research
-N
-P
-Ca
-K

## Slide 174
Why Are My Leaves Turning Yellow?
N
Mg
Fe
NO3
Nitrate
NH4
Ammonium
Top of
the Plant
Bottom of
the Plant
more on nutrient deficiencies

## Slide 175: N
Nitrogen deficiency initially resulted in lighter green color which proceeded to uniform chlorosis (yellowing) of older leaves. Reduced growth was noticeable within the first two weeks of exposure to the deficient conditions (A). Severe chlorosis of older leaves was observed after three weeks of deficient conditions (B)

## Slide 176: Mg
About 10 days after deficient conditions mature leaves exhibited light interveinal chlorosis (A) and shortly thereafter marginal necrosis was visible (B). After three weeks of Mg deficient conditions, all lower leaves exhibited severe interveinal chlorosis as well as marginal necrosis and some scattered necrotic spots along the leaf blade (C)

## Slide 177: Fe
Iron deficiency resulted in interveinal chlorosis of new growth within 10 days of exposure to deficient conditions (A). By the third week similar symptoms became more advanced on the plant and were presented on recently mature and younger leaves (B).

## Slide 178
THE END