## Slide 1
Insect to be excluded | Insect size micron / inch | Screen type to use | Screen opening micron (inch)
Leafminer | 640 / 0.025 | Vector-virus | 266 x 818 (0.0105 x 0.0322)
Melon Aphid | 340 / 0.013 |  | 
Whitefly | 462 / 0.018 |  | 
Western Flower Thrip | 192 / 0.0075 | No-Thrips | 150 x 150 (0.0059 x 0.0059)

## Slide 2
Specification | Anti-Virus | No-Thrips
Construction | 50 x 24 mesh | 81 x 81 mesh
Opening Size | 0.0105” x 0.0322” | 0.0059” x 0.0059”
Thread Size | 0.24 mm (240 micron) | 0.15 mm (150 micron)
Weave | 1/1 | 1/1
Weight | 0.33 lbs/yd | 0.216 lbs/yd
Shade value | 20% | 33%
Light Transmission | 80% | 66%
Standard Width | 43, 78, 118, 141 inches or custom widths | 39, 78 and 133 inches or custom widths
Maximum Length | 656 feet | 328 feet
UV resistance (equivalent to years of field experience) | 5 years | 3 years

## Slide 3
Insects common name | Width of thorax micron / inches | Width of abdomen micron / inches
Western flower Thrips | 215 / 0.0085 | 265 / 0.0104
Silverleaf Whitefly | 239 / 0.0094 | 565 / 0.0222
Greenhouse Whitefly | 288 / 0.0113 | 708 / 0.0279
Melon Aphid | 355 / 0.0140 | 2394 / 0.0549
Greenhouse Peach Aphid | 434 / 0.0171 | 2295 / 0.0904
Citrus Leafminer | 435 / 0.0171 | 810 / 0.0319
Serpentine Leafminer | 608 / 0.0239 | 850 / 0.0335

## Slide 4
Chart: Velocity, m/s

## Slide 5
Screen | Silverleaf Whitefly exclusion % efficiency Group |  | Thrips exclusion % efficiency Group |  | Air resistance
BugBed 123 | 93.6 | 1 | 93.3 | 1 | Moderate
No-Thrips | 86.8 | 2 | 94.8 | 1 | Very high
BugBed 110UV | 94.4 | 1 | 70.3 | 2 | Low
Econet S | 89.7 | 1 | 75.5 | 2 | High
BugBed 85 | 92.8 | 1 | 47.7 | 2 | Moderate
Econet T | 92.7 | 1 | 22.3 | 3 | High
Pak 52x52 | 93.9 | 1 | 4.2 | 3 | Moderate
Protex 1 | 92.9 | 1 | 30.4 | 3 | Low
Pak 44x44 | 77.8 | 2 | 36.4 | 2 | Moderate
Kontrol 45604 | 84.3 | 2 | 32.5 | 3 | Moderate
Lumite 52x52 | 86.2 | 2 | 32.5 | 3 | Moderate
Protex 2 | 88.1 | 2 | 25.9 | 3 | Moderate
Kontrol 45504 | 74.2 | 2 | 17.4 | 3 | Moderate
Typar | 61.1 | 2 | 25.1 | 3 | Very high
Anti-Virus | 73.1 | 2 | 18 | 3 | Moderate
Reemy | 72.1 | 2 | 14.1 | 3 | Moderate